## Slide 1: Unraveling Implosion Physics in Inertial Confinement Fusion: Direct-drive Simulations, Experiments, and Physics-Informed Data Science
P. B. Radha
Distinguished Scientist
Laboratory for Laser Energetics
University of Rochester
Seminar at MIPSE
University of Michigan
Nov 16, 2022

## Slide 2: Progress in direct drive implosion performance is being made through feedback between experiments and codes, and physics-informed data science techniques
Direct drive applications include studies related to high-energy density plasmas, nuclear astrophysics etc.
Several approaches in parallel are being pursued in parallel to improve performance in proof-of-principle DT-layered OMEGA implosions (kJ scale)
─ Surrogate implosions, targeted science experiments to guide design of cryogenic implosions and
improve simulation predictability
─ Improved tools for postprocessing simulations to identify signatures and potential
failure metrics
─ Data driven models incorporating failure metrics to improve performance
Modern computing is permitting large scale simulations with improved models.
Summary

## Slide 3: Collaborators
Laboratory for Laser Energetics, University of Rochester
General Atomics, San Diego
Lawrence Livermore National Labs
Plasma Science and Fusion Center, MIT
Los Alamos National Labs
Naval Research Labs, Washington DC
AWE, United Kingdom
University of Bordeaux

## Slide 4: Outline
Direct drive on OMEGA
Improving implosion performance by improving models
─ 1D physics – e.g. role of cross beam energy transfer and mitigation using laser bandwidth – evidence from the NIF – upgrade to ray-trace models in hydrodynamic simulations
─ multi-D physics – Role of perturbations - modeling and diagnosing nonuniformity
─ Postprocessing tools, new signatures identifying failure mechanisms
Improving implosion performance using physics informed data-science models
Scaling to Mega-Joule facilities

## Slide 5: Two primary laser driven approaches are being studied in the US
Review papers/books

## Slide 6: OMEGA implosion studies are based on hydrodynamic scaling between OMEGA and an ignition facility like the National Ignition Facility
E~R3
M~R3
P~R2
T~R

## Slide 7: The aim is drive implosions to develop conditions for a robust hotspot and propagating burn

## Slide 8: Lasers are used to set up the conditions for a hotspot and propagating burn

## Slide 9: Design parameters (adiabat and implosion velocity) are varied by varying targets and pulse shapes
Ice thickness is varied for
different implosion velocities

## Slide 10: A range of diagnostics are used to study the hot spot
rR~a-0.5

## Slide 11: Several measures of target performance indicating how close an implosion is to ignition have been identified

## Slide 12: Observations deviate from simulations with increasing convergence or decreasing adiabat
Yield degradation
(Measured yield/Simulated yield)
Areal density degradation
(Measured rR/Simulated rR)
Increasing convergence
Increasing convergence

## Slide 13: Implosion predictions are challenging because of the multi-scale and multi-physics involved

## Slide 14: Limited simulation predictability can be due to modeling errors, uncertainties in input to codes or engineering aspects not captured by codes

## Slide 15: Outline
Direct drive on OMEGA
Improving implosion performance by improving models
─ 1D physics – e.g. role of cross beam energy transfer and mitigation using laser bandwidth – evidence from the NIF – upgrade to ray-trace models in hydrodynamic simulations
─ multi-D physics – Role of perturbations - modeling and diagnosing nonuniformity
─ Postprocessing tools, new signatures identifying failure mechanisms
Improving implosion performance using physics informed data-science models
Scaling to Mega-Joule facilities

## Slide 16: Cross beam energy transfer can significantly reduce the ablation pressure
Phs = Hot spot pressure
Pa = Ablation pressure

## Slide 17: Laser deposition models in rad-hydro codes have been improved to include the effect of CBET

## Slide 18: Detuning the wavelengths of the crossing beams can improve ablation pressure as demonstrated on the NIF
J. Marozas et al, Phys. Rev. Lett (2018).

## Slide 19: NIF’s wavelength detuning capability has been used to demonstrate mitigation of CBET in proof-of-principle experiments

## Slide 20: Outline
Direct drive on OMEGA
Improving implosion performance by improving models
─ 1D physics – e.g. role of cross beam energy transfer and mitigation using laser bandwidth – evidence from the NIF – upgrade to ray-trace models in hydrodynamic simulations
─ multi-D physics – Role of perturbations - modeling and diagnosing nonuniformity
─ Postprocessing tools, new signatures identifying failure mechanisms
Improving implosion performance using physics informed data-science models
Scaling to Mega-Joule facilities

## Slide 21: Laser speckle can reduce the areal density for high IFAR implosions
P. B. Radha (DRACO - 2011)
15
30

## Slide 22: Highly resolved 3D simulations are now possible to model the effect of laser imprint
I. Igumenschev, PRL (2019)

## Slide 23: Outline
Direct drive on OMEGA
Improving implosion performance by improving models
─ 1D physics – e.g. role of cross beam energy transfer and mitigation using laser bandwidth – evidence from the NIF – upgrade to ray-trace models in hydrodynamic simulations
─ multi-D physics – Role of perturbations - modeling and diagnosing nonuniformity
─ Postprocessing tools, new signatures identifying failure mechanisms
Improving implosion performance using physics informed data-science models
Scaling to Mega-Joule facilities

## Slide 24: Hot spot flow, diagnosed by the Doppler shift in the DT neutron peak, can result in an inefficient conversion of the shell kinetic energy into hot spot energy

## Slide 25: Implosions with large flows also indicate asymmetries in the measured width of the neutron spectrum (apparent ion temperature variations)
O. Mannion (2019)
NtoF detectors
Flow

## Slide 26: Outline
Direct drive on OMEGA
Improving implosion performance by improving models
─ 1D physics – e.g. role of cross beam energy transfer and mitigation using laser bandwidth – evidence from the NIF – upgrade to ray-trace models in hydrodynamic simulations
─ multi-D physics – Role of perturbations - modeling and diagnosing nonuniformity
─ Postprocessing tools, new signatures identifying failure mechanisms
Improving implosion performance using physics informed data-science models
Scaling to Mega-Joule facilities

## Slide 27: Yield degradation mechanisms have been quantified through a multi-variate regression model with observed and simulated dependencies

## Slide 28: Multi-variate regression techniques are being used in parallel to identify quantities that determine implosion performance

## Slide 29
The statistical model predicts yield accurately and is used to design higher performing
implosions
The remaining scatter is due to
shot-to-shot variations in laser
delivery, target quality, and any
other design-dependent physics
that is not accounted for.

## Slide 30: Hydrodynamic scaling requires a modest increase in yield and areal density
C. Williams, Phys. Plasmas (2022).

## Slide 31: Outline
Direct drive on OMEGA
Improving implosion performance by improving models
─ 1D physics – e.g. role of cross beam energy transfer and mitigation using laser bandwidth – evidence from the NIF – upgrade to ray-trace models in hydrodynamic simulations
─ multi-D physics – Role of perturbations - modeling and diagnosing nonuniformity
─ Postprocessing tools, new signatures identifying failure mechanisms
Improving implosion performance using physics informed data-science models
Scaling to Mega-Joule facilities

## Slide 32: Many coronal processes influence laser energy deposition and electron transport to the ablation surface

## Slide 33: Progress in direct drive implosions is being made through feedback between experiments and codes, and physics-informed data science techniques
Direct drive applications include yield, studies related to stockpile stewardship, nuclear astrophysics, studies of matter under extreme conditions etc.
Several approaches in parallel are being pursued in parallel to improve performance in proof-of-principle DT-layered OMEGA implosions (kJ scale)
─ Surrogate implosions, targeted science experiments to guide design of cryogenic implosions and
improve simulation predictability
─ Improved tools for postprocessing simulations to identify signatures and potential
failure metrics
─ Data driven models incorporating failure metrics to improve performance
Modern computing is permitting large scale simulations with improved models.
Summary/Conclusions

## Slide 34
Coasting Phase

## Slide 35: Maintaining ablation pressure till the implosion bang time is key to improving compression

## Slide 36: The improved compression by maintaining ablation pressure has been demonstrated in OMEGA implosions
DD
n
He3
a
p (12-17 MeV)
Measured proton spectrum
Lines – Synthetic spectrum (IRIS)