## Slide 1: Plasma Lens for Active Optical Path Difference Control
T. Corke, B. Neiswander, E. Matlis
University of Notre Dame
Institute for Flow Physics and Control
Aerospace and Mechanical Engineering
Notre Dame, IN
University of Notre Dame
University of Michigan Institute for Plasma Science and Engineering
December 11, 2013
Notes: Introduce myself.

## Slide 2: Background
The topic of this seminar lies at the intersection of three generally independent disciplines: aerodynamics, plasma dynamics, and optics.
Aero-
dynamics
Optics
Plasma
Dynamics
PAO
PAO: Plasma Adaptive Optics

## Slide 3
Motivation: Aero-Optic Problem
Far-field Irradiance
Planar
Fluid Density Gradients
Aberrated
Near-field
Far-field
Laser Beam Aberrations
Planar
Aberrated
  Applies to laser communication and directed energy from moving aircraft
  Time-dependent density gradients in the boundary layer over the aircraft results in wave-front aberrations in the laser beam
  Aberrations cause a significant reduction in the on-target intensity (up to 70%).

## Slide 4: Aerodynamic Configuration
Separated flow imparts severe aero-optic disturbances to projected laser beam
Nose Turret

## Slide 5: Aero-Optics Correction Approach
Correction involves generating a conjugate waveform of the optical wavefront prior to its transmission through the aberrating fluid layer
The optical wavefront exiting the aberrating fluid layer is then transformed into a planar wavefront
Real-time correction requires 100kHz bandwidth!
Probing Beam

## Slide 6: Adaptive Aero-Optics
Aero-Optic
Disturbance
Deformable
Mirror
Sampler
Wave-front
Sensor
Computer
Laser
Near-field
Far-field
Signal
Reference

## Slide 7: Optics of Plasma
Gas discharge plasmas contain free electrons, neutrals, metastables, and ions
Consider neutrals, metastables and ions as “heavy particles”
Refractive index of plasma to electromagnetic radiation is

## Slide 8: Plasma Induced OPD
Optical path difference (OPD) is the equivalent length that an EM wave’s phase is advanced or lagged.
The maximum OPD determines how much adaptive optic correction is required
Plasma induced OPD depends on the length of the plasma, electron density, EM wavelength, gas composition, and heavy particle density
Fast electron OPD, slow heavy particle OPD

## Slide 9: Plasma Induced OPD
Aero-optic goal: 1μm OPDe at λ=1μm
Necessary plasma length
High electron density plasma
Minimize heavy particle OPD

## Slide 10
Plasma Adaptive Optic (PAO) Lens
Borosilicate tube
Transparent borosilicate tube of uniform wall thickness.

## Slide 11
Borosilicate tube
Optical glass
Optical glass attached and sealed to each end.
Gas pressure inside the tube is lowered.
Plasma Adaptive Optic (PAO) Lens

## Slide 12
Borosilicate tube
Optical glass
Electrode
Copper tape electrodes wrapped around the tube.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 13
Copper tape electrodes wrapped around the tube.
Borosilicate tube
Optical glass
Electrode
Low Pressure Gas
Dielectric (borosilicate)
Electrode
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 14
Borosilicate tube
Optical glass
Electrode
Copper tape electrodes wrapped around the tube.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 15
AC signal
Borosilicate tube
Optical glass
Electrode
AC voltage applied across the electrodes.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 16
AC signal
Borosilicate tube
Optical glass
Electrode
Plasma
Low pressure air breaks down and forms plasma.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 17
AC signal
Borosilicate tube
Optical glass
Electrode
Plasma
Dielectric barrier discharge (DBD): delayed transition to arcing,
operates in the glow regime.
Not a thermal plasma. Ionization is sustained by electron collisions.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 18
AC signal
Borosilicate tube
Optical glass
Electrode
Plasma
Plasma is an optically dispersive medium due to the interactions with
free electrons.
The refractive index is related to electron density and can be
controlled with the applied voltage potential.
.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 19
Laser
AC signal
Borosilicate tube
Optical glass
Electrode
Plasma
The PAO lens is an optical device with a controllable refractive index.
The optical path difference (OPD) created
depends on the length of plasma and the applied voltage.
Electrode
Plasma Adaptive Optic (PAO) Lens

## Slide 20: PAO Experimental Setup

## Slide 21: PAO Experimental Setup

## Slide 22: PAO Experimental Setup
A shift in the position of a specific interference fringe corresponds to OPD (in pixels):
Physical OPD takes into account the laser wavelength, λ:
For the interferometer, the average refractive index of the plasma lens with electrode spacing, d is:
Neglecting heavy particles, the dispersion eq. is:
Therefore an expression for the electron density is :
Finally, using a Buckinham-Pi analysis, an expression that relates electron density with the plasma lens input power, P, and pressure:

## Slide 23
Results: OPD Measurements
OPD Contours as a Function of Voltage
14kHz AC, 25.86 torr
10-6 m

## Slide 24
Results: OPD Measurements

## Slide 25
Multiple cells added to the PAO lens generates large OPD with low power consumption.
Array of multiple PAO lenses used for spatial wave-front correction.
The PAO lens could be modular.
Plasma Adaptive Optic (PAO) Lens

## Slide 26
Two plasma regimes occur depending on the d/D ratio.
A desire to miniaturize the PAO lens for lower power consumption and better modularity.
PAO Scaling

## Slide 27
Is there a critical d/D ratio for a centered plasma?
A desire to miniaturize the PAO lens for lower power consumption and better modularity.
PAO Scaling
Favored regime

## Slide 28
PAO lens with a variable electrode gap, d
Air inside lens at 0.5 psi (25.9 torr)
3 kV pk-pk, 14 kHz sine wave
Images acquired with 6 megapixel, 12-bit digital camera
Tested 12 different gap distances corresponding to 12 unique d/D ratios
Plasma
Position
adjustment knob
Optical window
Lead screw
Fixed electrode
Acrylic block
Borosilicate tube
Movable
electrode
Digital Camera
PAO Scaling: Experimental Setup
Notes: ADD dashed line of sight

## Slide 29
List of gap distances, d/D ratios, pd values, and
applied voltage potentials used in the experiment.
d, mm | d/D | p*d, Torr-cm | Voltage, kV
2.7 | 0.3 | 7.0 | 1.8
3.6 | 0.4 | 9.3 | 2.3
4.5 | 0.5 | 11.6 | 2.2
5.4 | 0.6 | 14.0 | 3.0
6.3 | 0.7 | 16.3 | 3.2
7.2 | 0.8 | 18.6 | 3.5
8.1 | 0.9 | 20.9 | 3.5
9.0 | 1 | 23.3 | 3.5
9.9 | 1.1 | 25.6 | 3.5
10.8 | 1.2 | 27.9 | 3.5
11.25 | 1.25 | 29.1 | 3.5
12.6 | 1.4 | 32.6 | 3.5
PAO Scaling: Experimental Conditions

## Slide 30
d/D = 0.3
0.7
1.1
0.4
0.8
1.2
0.5
0.9
1.25
0.6
1.0
1.4
Plasma Luminescence
PAO Scaling: Experiment Images

## Slide 31
(1) Load raw tiff image.
(2) Crop and remove color
channels.
(3) Threshold image. Detect diameter and center.
(4) Extract 360° radial slices
(5) Average slices, calculate
max, min, inflection locations
(6) Form radially averaged
image
PAO Scaling: Image Processing

## Slide 32
d/D = 0.3
0.7
1.1
0.4
0.8
1.2
0.5
0.9
1.25
0.6
1.0
1.4
Azimuthally Averaged Plasma Luminescence
PAO Scaling: Image Results

## Slide 33
Voltage Potential:
Electric Field Components:
Electrostatic equations for the voltage and electric field in the x-z plane induced by a charged ring lying in the x-y plane.
PAO Scaling: Electrostatic Analysis

## Slide 34
Positive ring at
z = d/2.
Solution
domain (z=0)
Negative ring at
z = -d/2.
Superposition of two oppositely charged rings of diameter D a distance d apart.
PAO Lens Model:
Model neglects dielectrics, space charges, electrode length, and AC.
PAO Scaling: Electrostatic Analysis

## Slide 35
d/D = 0.3
0.7
1.1
0.4
0.8
1.2
0.5
0.9
1.25
0.6
1.0
1.4
Contours of Electric Field Magnitude
PAO Scaling: Electrostatic Analysis

## Slide 36
Experiment gave profiles of plasma luminescence.
Theory gave profiles of electric field magnitude.
Regions of high electric field are presumed to be associated with high plasma ionization and luminescence.
We compare the locations of maximum plasma luminescence and maximum electric field magnitude.
Experiment
Theory
0.7
0.7
Plasma
Luminescence
Electric Field
Magnitude
PAO Scaling: Validation

## Slide 37
PAO Scaling: Validation

## Slide 38
Extract radial profile,
Normalize by total radius.
PAO Scaling: Validation

## Slide 39
Extract radial profile,
Normalize by total radius.
Determine the location
of maximum, .
PAO Scaling: Validation

## Slide 40
Extract radial profile,
Normalize by total radius.
Determine the location
of maximum, .
We obtain a single point,
PAO Scaling: Validation

## Slide 41
PAO Scaling: Validation
Critical d/D = 1.22.

## Slide 42
PAO Scaling: Theory
Critical d/D = 1.22.

## Slide 43
PAO Scaling: Theory
Critical d/D = 1.22.

## Slide 44
PAO Scaling: Theory
Critical d/D = 1.22.

## Slide 45
There is some discrepancy between experiment and theory comparison.
Extra inflections are found in the experimental data.
PAO Scaling: Theory
Extra
Inflection

## Slide 46
Renormalize experimental data by first inflection point.
PAO Scaling: Theory

## Slide 47
4. Discussion
Comparison
New normalization
improves agreement.
Critical d/D = 1.22.

## Slide 48: Summary
  Optimized a dielectric barrier plasma geometry plasma lens and directly measured OPD
  The experiment validated an electron density model that neglected the effect of heavy particles
  A simple charged ring electric field model reproduced the experimental results of a critical d/D=1.22 for a centered plasma in the cylindrical plasma lens design.
  Developing a new plasma diagnostic technique (Phase Sensitive FTIR Interferometry) to determine the contributions of electron and heavy particle contributions to the OPD.
B. Neiswander, E. Matlis and T. Corke, AIAA J., 50, 1, 123-130 (2012).
B. Neiswander, E. Matlis and T. Corke, AIAA J., 51, 3, 657-664 (2013).

## Slide 49: Phase Sensitive FTIR Interferometry
  Blackbody source emits broadband infrared spectrum
  Michelson interferometer with motorized moving mirror
  Mirror location amplified and attenuates certain wavelengths
  700-1250cm-1 (8-12μm), 4cm-1 resolution
  Measures absorption spectroscopy, dispersion profile, OPD, electron and heavy particle density

## Slide 50: Phase Sensitive FTIR Interferometry Analysis

## Slide 51: Phase Sensitive FTIR Interferometry Simulation

## Slide 52: References
B. Neiswander, E. Matlis and T. Corke, AIAA J., Vol 50, No. 1, pp. 123-130 (2012).
B. Neiswander, E. Matlis and T. Corke, AIAA J., Vol 51, No. 3, pp. 657-664 (2013).

## Slide 53: Plasma Optics
Assumptions:
Optical probing frequency >> plasma frequency
Attenuation of probing beam is negligible (probing frequency >> collision frequency)
Probing wave is monochromatic
Unity relative permittivity.
Optical Probing Frequency
Plasma Frequency
Refractive Index
Free Electrons
Heavy Particles

## Slide 54
D
d
Small d/D:
Surface plasma
regime
Large d/D:
Centered plasma
regime
Gap-Diameter Ratio: d/D
Two plasma regimes occur depending on the d/D ratio.
A desire to miniaturize the PAO lens for lower power consumption and better modularity.
PAO Scaling

## Slide 55
Small d/D:
Surface plasma
regime
Large d/D:
Centered plasma
regime
Center plasma regime produces coalesced area of concentrated plasma.
Favored regime
Determine the critical d/D ratio
between a surface and center plasma.
Objective:
PAO Scaling