## Slide 1: How ignition and target gain > 1 was achieved in inertial fusion
O. A. Hurricane (Indirect Drive ICF Collaboration)
MIPSE
Wednesday, March 8st, 2023
3:30 pm, Ann Arbor Michigan

## Slide 2: Recent NIF ICF experiments are an “existence proof” of laboratory ignition and “target gain” (Gtarget>1)
No mystery physics obstacle stands in the way of ignition (explosive thermodynamic instability) or gain (energy out > energy in)
The theoretical prediction of the physics parameter regime (e.g. Lawson triple product) where ignition was expected is consistent with our results
Additional laser energy (at fixed power) was very beneficial
Implosion physics was more sensitive to engineering control of the laser and targets than originally thought
So far, very high gain (high compression) target designs have not worked as expected. All break-throughs over the past decade have used low gain designs
Remarkable that we can now talk about burning plasmas, ignition, and scientific breakeven in the past-tense!

## Slide 3: In order to get high fusion yields, we need to assemble the fusion fuel into a configuration that can stop alpha’s in the fusion plasma
heat
heat
helium-4 nuclei
Fusion reaction:
approximation to DT reaction-rate
Reaction-rate
70-80% α’s stopped in “hotspot” increasing T
20-30% α’s ablate fuel increasing hotspot mass
Conditions needed:
hotspot areal density ()
peak central density ()
pressure (
DT
If these condition are met, a thermal feed-back loop, “ignition,” is generated
“Self-heating”

## Slide 4: Indirect drive inertial confinement fusion (ICF) uses x-rays to ablate and accelerate a capsule of fusion fuel to extreme velocity
e.g. Nuckolls, et al, Nature, 1972; Lindl, Phys. Plasma, 1995; Haan, et al., PoP, 2011
Lasers deposit energy into hohlraum
A bath of x-rays is created as the hohlraum heats
The capsule surface ablates at ~150 Mbar
Capsule accelerates inwards doing pdV work
Kinetic energy is converted into internal energy
“Implosion”
“Stagnation”

## Slide 5: Often conflated, the terms “burning plasma,” “ignition,” and “gain” all mean something physically different
Burning plasma*
  ICF: Self-heating energy exceeds external “pdV work” to heat and compress the DT
  MFE: Self-heating energy exceeds external heating of the DT
Ignition (i.e. Lawson Criterion† )
  Self-heating power exceeds all DT plasma power losses
    Losses are radiative, electron heat conduction, negative pdV work
  Results in thermodynamic instability (explosive increase in T, Y, etc).
Target Gain
  Fusion yield exceeds laser energy into target
  1997 NAS committee used this as “ignition” in a report & the U.S. DOE adopted this definition
*Betti, et al, PRL, 2015; †Lawson, J.D., Proc. Phys. Soc., B, 1957

## Slide 6: 96 laser beams
96 laser beams
300-400 MJ electrical energy into capacitor banks
The National Ignition Facility (NIF)
Notes: Should say 1 or 2 sentence about mission of NIF -- stockpile stewardship

## Slide 7: 96 laser beams
96 laser beams
The NIF delivers delivers frequency tripled (3⍵) laser light into the target chamber
3 MJ of red light just before target chamber
Notes: Should say 1 or 2 sentence about mission of NIF -- stockpile stewardship

## Slide 8: 96 laser beams
96 laser beams
The 3⍵ light is what enters the ICF target
2 MJ of blue light→
Notes: Should say 1 or 2 sentence about mission of NIF -- stockpile stewardship

## Slide 9: 96 laser beams
96 laser beams
Laser light is converted into a bath of x-rays that ablate the capsule
250 kJ x-ray absorbed by capsule
↓
300-400 MJ electrical energy into capacitor banks
Notes: Should say 1 or 2 sentence about mission of NIF -- stockpile stewardship

## Slide 10: 96 laser beams
96 laser beams
Inertial fusion sacrifices energy for energy density
2 MJ of blue light→
250 kJ x-ray absorbed by capsule
↓
20 kJ internal energy into DT fuel inside capsule
Most of the initial energy is lost before any gets to the fusion fuel
300-400 MJ electrical energy into capacitor banks
Notes: Should say 1 or 2 sentence about mission of NIF -- stockpile stewardship

## Slide 11: There are several energy gain metrics in ICF, all increased by approximately 5000x over the past decade on the NIF
Chart: 
Theory | 0.010007 | 0.020028 | 0.030063 | 0.040112 | 0.050176 | 0.060253 | 0.070345 | 0.080451 | 0.090571 | 0.1007 | 0.20284 | 0.30644 | 0.41152 | 0.51813 | 0.6263 | 0.73607 | 0.84746 | 0.96051 | 1.0753 | 2.3256 | 3.7975 | 5.5556 | 7.6923 | 10.3448 | 13.7255 | 18.1818 | 24.3243 | 33.3333 | 47.8261 | 75 | 144.4444 | 700
(early 2014)
N221204
N210808
Target
Capsule/Ablator
Fuel
~1 cm
N120422
Theory*
After 10 years and as of Dec. 5, 2022
Gtarget ~ 1.5
Gcapsule ~ 12
Gfuel ~ 160
Gtarget > 1 is not “net energy gain,” because of facility energy consumption
(mid 2021)
(end 2022)
*Hurricane, et al, RMP in press, 2023
Generalized Lawson Criterion (GLC) – atm-s & keV units
ignited

## Slide 12: It took a decade of work to tackle several key target physics challenges that frustrated our progress
Instability control
Symmetry control
Sufficient energy coupling
Target quality
Ultra-high compression

## Slide 13: In indirect-drive, the hohlraum, ablator, and laser pulse determine the ablation pressure that drives the implosion
Key elements of ICF laser pulse:
Foot – controls stability and majority of fuel entropy (adiabat, )
Peak Power – implosion velocity
Coast period – efficiency of KE conversion into DT internal energy, via radius of peak velocity
1
2
3
Ablator material that forms capsule
Hohlraum and laser pulse-shape
Ablation pressure on implosion:

## Slide 14: 2010-12: Plastic ablator “Low-foot” implosions were designed to be high yield ( > 1 MJ), but underperformed for many reasons*
Chart: DD Tion (keV)
| 2.8166523399999996 | 3.10177755 | 3.7102224349999999 | 1.9656060500000001 | 2.2562298599999999 | 2.3196550899999999 | 3.2306102800000001 | 3.0590000000000002 | 3.42 | 3.0874999999999999 | 2.698 | 3.1196316599999996 | 3.1825000000000001 | 1.482 | 2.4129999999999998 | 1.7694832999999999 | 2.16019797 | 2.6512360599999996 | 1.2961119799999998 | 1.4681817749999999 | 2.58324665 | 1.5718612599999999 | 1.52 | 1.9664999999999997 | 1.823855885 | 2.3198154500000001 | 2.0139999999999998 | 2.8982476500000001 | 2.3524722699999998
Lowfoot | 2.3007e+14 | 4.9853e+14 | 4.9268e+14 | 2.0131e+14 | 5.4208e+14 | 7.0044e+14 | 7.0125e+14 | 2.671e+14 | 6.6739e+14 | 8.9073e+14 | 3.7191e+14 | 718077391559984 | 6.6947e+14 | 114506738445614 | 417573826559862 | 1.5884e+14 | 2.7533e+14 | 5.3601e+14 | 1.5712e+14 | 1.3491e+14 | 5.3264e+14 | 9.9416e+13 | 1.1848e+14 | 2.962e+14 | 1.9182e+14 | 3.6208e+14 | 1.8334e+14 | 5.5419e+14 | 3.5005e+14
Chart: Hot spot peak pressure (Gbar)
| 36.300390418507163 | 38.201815644096094 | 73.540545281612395 | 88.478314699521903 | 100.38498481154691 | 77.56558155614411 | 89.899370104105657 | 81.324287847115812 | 81.195003667948043 | 82.841709981997823 | 74.893791487041838 | 108.01484490028928 | 95.965986858869897 | 101.70938529975722 | 105.56478533690347 | 102.59436226562764 | 77.558365829556152 | 56.630182685752466 | 102.26762536234986 | 78.004036611990415 | 68.783167527125826 | 64.722289545101617 | 73.39828854496929 | 91.266462842672311
Lowfoot | 0.6497 | 1.4078 | 1.3913 | 0.56846 | 1.5308 | 1.978 | 1.9802 | 0.75427 | 1.8846 | 2.5153 | 1.0502 | 2.0278 | 1.8905 | 0.32335 | 1.1792 | 0.44856 | 0.77748 | 1.5136 | 0.44368 | 0.38096 | 1.5041 | 0.28074 | 0.33458 | 0.83642 | 0.54166 | 1.0225 | 0.51774 | 1.565 | 0.9885
*Edwards, et al, PoP, 2013; Ma, et al., PoP, 2013; Regan et al, PRL, 2013; Lindl, et al., PoP, 2014; Clark, et al, PoP, 2016

## Slide 15: Hydro-dynamic instability defeats density and temperature gradients and is more challenging with higher compression
D. Clark et al., Phys. Plasmas 23, 056302 (2016)
Tion
⍴
“Takabe” formula for linear growth rate:
Numerous forms: e.g. Bodner, Betti, Kilkenny, Takabe, etc.
acceleration (g) is destabilizing
(but how else to get high vimp?)
long density gradient scale help
high ablation velocity () helps
Lead to “high foot” implosion
Exponential perturbation growth:
wavelength,
“Rayleigh-Taylor” (RT)

## Slide 16: 2013-2015: High-foot implosions tested if better controlling hydrodynamic instability would improve performance
Chart: DD Tion (keV)
| 2.8166523399999996 | 3.10177755 | 3.7102224349999999 | 1.9656060500000001 | 2.2562298599999999 | 2.3196550899999999 | 3.2306102800000001 | 3.0590000000000002 | 3.42 | 3.0874999999999999 | 2.698 | 3.1196316599999996 | 3.1825000000000001 | 1.482 | 2.4129999999999998 | 1.7694832999999999 | 2.16019797 | 2.6512360599999996 | 1.2961119799999998 | 1.4681817749999999 | 2.58324665 | 1.5718612599999999 | 1.52 | 1.9664999999999997 | 1.823855885 | 2.3198154500000001 | 2.0139999999999998 | 2.8982476500000001 | 2.3524722699999998
Lowfoot | 2.3007e+14 | 4.9853e+14 | 4.9268e+14 | 2.0131e+14 | 5.4208e+14 | 7.0044e+14 | 7.0125e+14 | 2.671e+14 | 6.6739e+14 | 8.9073e+14 | 3.7191e+14 | 718077391559984 | 6.6947e+14 | 114506738445614 | 417573826559862 | 1.5884e+14 | 2.7533e+14 | 5.3601e+14 | 1.5712e+14 | 1.3491e+14 | 5.3264e+14 | 9.9416e+13 | 1.1848e+14 | 2.962e+14 | 1.9182e+14 | 3.6208e+14 | 1.8334e+14 | 5.5419e+14 | 3.5005e+14
Highfoot | 8.6358e+14 | 6.3932e+14 | 1195303212552838 | 5.3786e+14 | 2.784e+15 | 5053722543452773 | 5959595564216789 | 3457388933441035 | 9247294435034856 | 3.213e+15 | 9212715514096852 | 6049984620508881 | 7112184639304813 | 9008657158494278 | 4946812097430978 | 6237640532699912 | 5471636750709320 | 3.5665e+15 | 3.2185e+15 | 7233783891383544 | 8670326219332719 | 5762823827312619 | 5533608524370136 | 6683306150932161 | 8095378221881889 | 6818474297884493 | 3087425113360610 | 5602244302685341 | 4.389e+15 | 6316168264117427 | 3313826289796072 | 10711842442947206 | 2803891516187706 | 4729047336431093
Chart: Hot spot peak pressure (Gbar)
| 36.300390418507163 | 38.201815644096094 | 73.540545281612395 | 88.478314699521903 | 100.38498481154691 | 77.56558155614411 | 89.899370104105657 | 81.324287847115812 | 81.195003667948043 | 82.841709981997823 | 74.893791487041838 | 108.01484490028928 | 95.965986858869897 | 101.70938529975722 | 105.56478533690347 | 102.59436226562764 | 77.558365829556152 | 56.630182685752466 | 102.26762536234986 | 78.004036611990415 | 68.783167527125826 | 64.722289545101617 | 73.39828854496929 | 91.266462842672311
Lowfoot | 0.6497 | 1.4078 | 1.3913 | 0.56846 | 1.5308 | 1.978 | 1.9802 | 0.75427 | 1.8846 | 2.5153 | 1.0502 | 2.0278 | 1.8905 | 0.32335 | 1.1792 | 0.44856 | 0.77748 | 1.5136 | 0.44368 | 0.38096 | 1.5041 | 0.28074 | 0.33458 | 0.83642 | 0.54166 | 1.0225 | 0.51774 | 1.565 | 0.9885
Highfoot | 2.4387 | 1.8054 | 3.3754 | 1.5188 | 7.8617 | 14.2711 | 16.8292 | 9.7632 | 26.1132 | 9.0732 | 26.0156 | 17.0844 | 20.0839 | 25.4393 | 13.9692 | 17.6143 | 15.4512 | 10.0713 | 9.0885 | 20.4273 | 24.4839 | 16.2735 | 15.6262 | 18.8728 | 22.8604 | 19.2545 | 8.7185 | 15.8201 | 12.394 | 17.8361 | 9.3578 | 30.2489 | 7.9178 | 13.3543
Hinkel, et al. PPCF, 2013; Dittrich, et al. PRL, 2014; Park, et al., PRL, 2014; Hurricane, et al., Nature, 2014

## Slide 17: While the high foot implosions increased fusion yield by 10x and had repeatable behavior, symmetry control was an issue
Spears, et al., PoP, 2014; Ma, et al, PRL, 2016; Hurricane, et al, Nat. Phys, 2016
350 TW & 1.6 MJ
390 TW & 1.8 MJ

## Slide 18: Series of high-foot experiments revealed the importance of “coast-time” in maximizing mechanical power transfer
Coast-time ~ duration between max compression and end of laser pulse
Radius of peak velocity, , minimized with short coast-time
Hurricane, et al, PoP, 2017; Hurricane, et al, PoP, 2022
“Late braking”

## Slide 19: 2015-2018: Higher pressures achieved using high density carbon ablators and low gas-fill hohlraums
Chart: DD Tion (keV)
| 2.8166523399999996 | 3.10177755 | 3.7102224349999999 | 1.9656060500000001 | 2.2562298599999999 | 2.3196550899999999 | 3.2306102800000001 | 3.0590000000000002 | 3.42 | 3.0874999999999999 | 2.698 | 3.1196316599999996 | 3.1825000000000001 | 1.482 | 2.4129999999999998 | 1.7694832999999999 | 2.16019797 | 2.6512360599999996 | 1.2961119799999998 | 1.4681817749999999 | 2.58324665 | 1.5718612599999999 | 1.52 | 1.9664999999999997 | 1.823855885 | 2.3198154500000001 | 2.0139999999999998 | 2.8982476500000001 | 2.3524722699999998
Lowfoot | 2.3007e+14 | 4.9853e+14 | 4.9268e+14 | 2.0131e+14 | 5.4208e+14 | 7.0044e+14 | 7.0125e+14 | 2.671e+14 | 6.6739e+14 | 8.9073e+14 | 3.7191e+14 | 718077391559984 | 6.6947e+14 | 114506738445614 | 417573826559862 | 1.5884e+14 | 2.7533e+14 | 5.3601e+14 | 1.5712e+14 | 1.3491e+14 | 5.3264e+14 | 9.9416e+13 | 1.1848e+14 | 2.962e+14 | 1.9182e+14 | 3.6208e+14 | 1.8334e+14 | 5.5419e+14 | 3.5005e+14
Highfoot | 8.6358e+14 | 6.3932e+14 | 1195303212552838 | 5.3786e+14 | 2.784e+15 | 5053722543452773 | 5959595564216789 | 3457388933441035 | 9247294435034856 | 3.213e+15 | 9212715514096852 | 6049984620508881 | 7112184639304813 | 9008657158494278 | 4946812097430978 | 6237640532699912 | 5471636750709320 | 3.5665e+15 | 3.2185e+15 | 7233783891383544 | 8670326219332719 | 5762823827312619 | 5533608524370136 | 6683306150932161 | 8095378221881889 | 6818474297884493 | 3087425113360610 | 5602244302685341 | 4.389e+15 | 6316168264117427 | 3313826289796072 | 10711842442947206 | 2803891516187706 | 4729047336431093
HDC | 5.3597e+14 | 1.7963e+15 | 1712664650695105 | 2.8645e+15 | 3.1245e+15 | 5238516636221929 | 2.1943e+15 | 7407405694437828 | 16488410188316704 | 9932156315524684 | 18827464044589872 | 17075549838955372 | 16941525813787744 | 11759705394782046 | 9176806260598032 | 11918661284430708 | 18098118121775908 | 15290284318391468 | 17529354646190830 | 11800628003475570 | 18828885893439072 | 10298114522134856 | 12988951744342700 | 11928164346638864
Bigfoot | 1.8565e+15 | 2.6028e+15 | 7490982936074811 | 10943626537285760 | 6233927031704696 | 7956920550468615 | 10268569444661902 | 11243077854423324 | 19571038072255672 | 10767125212399366 | 10157188017659130 | 13811493691834616 | 17217470464129840 | 7219011028228234 | 17331493555461886
Chart: Hot spot peak pressure (Gbar)
| 36.300390418507163 | 38.201815644096094 | 73.540545281612395 | 88.478314699521903 | 100.38498481154691 | 77.56558155614411 | 89.899370104105657 | 81.324287847115812 | 81.195003667948043 | 82.841709981997823 | 74.893791487041838 | 108.01484490028928 | 95.965986858869897 | 101.70938529975722 | 105.56478533690347 | 102.59436226562764 | 77.558365829556152 | 56.630182685752466 | 102.26762536234986 | 78.004036611990415 | 68.783167527125826 | 64.722289545101617 | 73.39828854496929 | 91.266462842672311
Lowfoot | 0.6497 | 1.4078 | 1.3913 | 0.56846 | 1.5308 | 1.978 | 1.9802 | 0.75427 | 1.8846 | 2.5153 | 1.0502 | 2.0278 | 1.8905 | 0.32335 | 1.1792 | 0.44856 | 0.77748 | 1.5136 | 0.44368 | 0.38096 | 1.5041 | 0.28074 | 0.33458 | 0.83642 | 0.54166 | 1.0225 | 0.51774 | 1.565 | 0.9885
Highfoot | 2.4387 | 1.8054 | 3.3754 | 1.5188 | 7.8617 | 14.2711 | 16.8292 | 9.7632 | 26.1132 | 9.0732 | 26.0156 | 17.0844 | 20.0839 | 25.4393 | 13.9692 | 17.6143 | 15.4512 | 10.0713 | 9.0885 | 20.4273 | 24.4839 | 16.2735 | 15.6262 | 18.8728 | 22.8604 | 19.2545 | 8.7185 | 15.8201 | 12.394 | 17.8361 | 9.3578 | 30.2489 | 7.9178 | 13.3543
HDC | 1.5135 | 5.0726 | 4.8364 | 8.0891 | 8.8232 | 14.7929 | 6.1965 | 20.9176 | 46.5613 | 28.0472 | 53.1665 | 48.2193 | 47.8408 | 33.208 | 25.9142 | 33.6568 | 51.1069 | 43.1779 | 49.5008 | 33.3235 | 53.1705 | 29.0806 | 36.6792 | 33.6837
Bigfoot | 5.2425 | 7.3501 | 21.1536 | 30.9035 | 17.6038 | 22.4694 | 28.9972 | 31.7491 | 55.2662 | 30.405 | 28.6827 | 39.002 | 48.62 | 20.3856 | 48.942
Divol, et al, PoP, 2017; LePape, et al, PRL, 2018; Berzak-Hopkins, et al, PPCF, 2018; Casey, et al, PoP, 2018; Baker, et al, PRL, 2018; Thomas, et al., PoP, 2020

## Slide 20: Symmetry control was improved with HDC ablators and low gas-fill hohlraums, but control is still challenging, even today
e.g. Kritcher, et al., Nature Phys. 18, 251 (2022)
Data
Synthetic data from simulation
HYDRA*
Simulation
*Marinak, et al., PoP, 2003

## Slide 21: In ICF, it is essential to maximize the conversion of implosion kinetic energy into hotspot internal energy
Experimental scaling of fusion yield with hotspot energy, Y ~ E3.3
Chart: 
| 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Analytic Model | 0.96705 | 0.93488 | 0.90345 | 0.87278 | 0.84284 | 0.81363 | 0.78513 | 0.75734 | 0.73025 | 0.70384 | 0.4753 | 0.30455 | 0.18218 | 0.099213 | 0.047156 | 0.018075 | 0.0046784 | 0.00046416 | 0
5th power | 0.9479 | 0.89822 | 0.85084 | 0.80568 | 0.76263 | 0.72162 | 0.68256 | 0.64537 | 0.60996 | 0.57626 | 0.3186 | 0.16714 | 0.081859 | 0.036498 | 0.014203 | 0.0044572 | 0.00094456 | 7.6725e-05 | 0
High-foot Postshots | 0.85193 | 0.35652 | 0.43953 | 0.73903 | 0.42215 | 0.68421 | 0.45788 | 0.57122 | 0.65179 | 0.63883 | 0.72727 | 0.72031 | 0.77224
Simulations:
▲ Burn-off LF from Kritcher, et al., PoP, 2014
◼︎ Burn-on LF from Kritcher, et al., PoP, 2014
⚫️ Burn-on HF from Kritcher, et al., PoP, 2016
Degradation of fusion yield with asymmetry, Y ~ (1-nRKE)3.3
Burn-off piston model
Burn-on piston model
Ehs(kJ)
Total Fusion Neutron Yield
“HYBRID” strategy: [Hurricane, et al., PPCF 61, 014033 (2018); PoP 26, 052704 (2019)]
KE split into hotspot,
Increased asymmetry
Decreased asymmetry
Ehs, KE, & symmetry connected:

## Slide 22: Implosion symmetry control is important, because it wastes kinetic energy, that could have heated the fusion fuel
Asymmetric implosion abstracted to pistons
Center-of-mass motion
hot
plasma
From conservation of energy and momentum:
minimum hot volume
“wasted” KE
Mode-1:
Wasted KE = “residual kinetic energy (RKE)”
Hurricane, et al, PoP, 2020, Casey, et al, PRL, 2021; MacGowan, et al, HEDP, 2022

## Slide 23: Asymmetry wastes kinetic energy, even when there is no net center of mass motion – geometry is a reflection of energy
Mode-2:
WHM = weighted harmonic mean* of shell areal density
Key parameter for 3D asymmetry:
Legendre mode 2
*Hurricane, et al, PoP, 2022; Betti & Woo, PoP, 2021

## Slide 24: Significantly improved understanding of the levers controlling implosion symmetry obtained during the 2015-2018 period
Callahan, et al., PoP, 2018;
Ralph, et al, PoP, 2018
Legendre mode-2 (“P2”) scaling:
Cross-beam energy transfer with low gas-fill:
A. L. Kritcher, et al Phys. Rev. E 98, 053206 (2018); L. Pickworth, et al, PoP (2020)
Å
Å
Beam pointing has limited control

## Slide 25: 2018-2020: With a better understanding of the levers on capsule and hohlraum control, we scaled up capsule radius, but ...
Chart: DD Tion (keV)
| 2.8166523399999996 | 3.10177755 | 3.7102224349999999 | 1.9656060500000001 | 2.2562298599999999 | 2.3196550899999999 | 3.2306102800000001 | 3.0590000000000002 | 3.42 | 3.0874999999999999 | 2.698 | 3.1196316599999996 | 3.1825000000000001 | 1.482 | 2.4129999999999998 | 1.7694832999999999 | 2.16019797 | 2.6512360599999996 | 1.2961119799999998 | 1.4681817749999999 | 2.58324665 | 1.5718612599999999 | 1.52 | 1.9664999999999997 | 1.823855885 | 2.3198154500000001 | 2.0139999999999998 | 2.8982476500000001 | 2.3524722699999998
Lowfoot | 2.3007e+14 | 4.9853e+14 | 4.9268e+14 | 2.0131e+14 | 5.4208e+14 | 7.0044e+14 | 7.0125e+14 | 2.671e+14 | 6.6739e+14 | 8.9073e+14 | 3.7191e+14 | 718077391559984 | 6.6947e+14 | 114506738445614 | 417573826559862 | 1.5884e+14 | 2.7533e+14 | 5.3601e+14 | 1.5712e+14 | 1.3491e+14 | 5.3264e+14 | 9.9416e+13 | 1.1848e+14 | 2.962e+14 | 1.9182e+14 | 3.6208e+14 | 1.8334e+14 | 5.5419e+14 | 3.5005e+14
Highfoot | 8.6358e+14 | 6.3932e+14 | 1195303212552838 | 5.3786e+14 | 2.784e+15 | 5053722543452773 | 5959595564216789 | 3457388933441035 | 9247294435034856 | 3.213e+15 | 9212715514096852 | 6049984620508881 | 7112184639304813 | 9008657158494278 | 4946812097430978 | 6237640532699912 | 5471636750709320 | 3.5665e+15 | 3.2185e+15 | 7233783891383544 | 8670326219332719 | 5762823827312619 | 5533608524370136 | 6683306150932161 | 8095378221881889 | 6818474297884493 | 3087425113360610 | 5602244302685341 | 4.389e+15 | 6316168264117427 | 3313826289796072 | 10711842442947206 | 2803891516187706 | 4729047336431093
HDC | 5.3597e+14 | 1.7963e+15 | 1712664650695105 | 2.8645e+15 | 3.1245e+15 | 5238516636221929 | 2.1943e+15 | 7407405694437828 | 16488410188316704 | 9932156315524684 | 18827464044589872 | 17075549838955372 | 16941525813787744 | 11759705394782046 | 9176806260598032 | 11918661284430708 | 18098118121775908 | 15290284318391468 | 17529354646190830 | 11800628003475570 | 18828885893439072 | 10298114522134856 | 12988951744342700 | 11928164346638864
Bigfoot | 1.8565e+15 | 2.6028e+15 | 7490982936074811 | 10943626537285760 | 6233927031704696 | 7956920550468615 | 10268569444661902 | 11243077854423324 | 19571038072255672 | 10767125212399366 | 10157188017659130 | 13811493691834616 | 17217470464129840 | 7219011028228234 | 17331493555461886
HyE 1100 | 7487396477244934 | 19054577441139372 | 20273661169132376 | 5633721647119410 | 14444780994508152 | 6582032860372935 | 14306884129055594 | 6560353168367902 | 18092074881857056
Iraum | 6747266238726404 | 17825174083221002 | 17808213002747668 | 37685194612347104 | 56983885401791256 | 24132771452484060
Chart: Hot spot peak pressure (Gbar)
| 36.300390418507163 | 38.201815644096094 | 73.540545281612395 | 88.478314699521903 | 100.38498481154691 | 77.56558155614411 | 89.899370104105657 | 81.324287847115812 | 81.195003667948043 | 82.841709981997823 | 74.893791487041838 | 108.01484490028928 | 95.965986858869897 | 101.70938529975722 | 105.56478533690347 | 102.59436226562764 | 77.558365829556152 | 56.630182685752466 | 102.26762536234986 | 78.004036611990415 | 68.783167527125826 | 64.722289545101617 | 73.39828854496929 | 91.266462842672311
Lowfoot | 0.6497 | 1.4078 | 1.3913 | 0.56846 | 1.5308 | 1.978 | 1.9802 | 0.75427 | 1.8846 | 2.5153 | 1.0502 | 2.0278 | 1.8905 | 0.32335 | 1.1792 | 0.44856 | 0.77748 | 1.5136 | 0.44368 | 0.38096 | 1.5041 | 0.28074 | 0.33458 | 0.83642 | 0.54166 | 1.0225 | 0.51774 | 1.565 | 0.9885
Highfoot | 2.4387 | 1.8054 | 3.3754 | 1.5188 | 7.8617 | 14.2711 | 16.8292 | 9.7632 | 26.1132 | 9.0732 | 26.0156 | 17.0844 | 20.0839 | 25.4393 | 13.9692 | 17.6143 | 15.4512 | 10.0713 | 9.0885 | 20.4273 | 24.4839 | 16.2735 | 15.6262 | 18.8728 | 22.8604 | 19.2545 | 8.7185 | 15.8201 | 12.394 | 17.8361 | 9.3578 | 30.2489 | 7.9178 | 13.3543
HDC | 1.5135 | 5.0726 | 4.8364 | 8.0891 | 8.8232 | 14.7929 | 6.1965 | 20.9176 | 46.5613 | 28.0472 | 53.1665 | 48.2193 | 47.8408 | 33.208 | 25.9142 | 33.6568 | 51.1069 | 43.1779 | 49.5008 | 33.3235 | 53.1705 | 29.0806 | 36.6792 | 33.6837
Bigfoot | 5.2425 | 7.3501 | 21.1536 | 30.9035 | 17.6038 | 22.4694 | 28.9972 | 31.7491 | 55.2662 | 30.405 | 28.6827 | 39.002 | 48.62 | 20.3856 | 48.942
HyE 1100 | 21.1435 | 53.8078 | 57.2503 | 15.9089 | 40.7903 | 18.5869 | 40.4009 | 18.5256 | 51.0898
Iraum | 19.0535 | 50.3361 | 50.2882 | 106.4184 | 160.9155 | 68.148
... initially this strategy struggled
HyE 1100: Zylstra, et al, PRL, 2019; Kritcher et al., PoP, 2020
I-raum: Robey, et al, PoP, 2018; Ross, et al, arXiv, 2021

## Slide 26: We got surprised by numerous capsule defects when we increased capsule radius ... problems identified (as shown) and eventually resolved
Slide courtesy T. Braun, LLNL target fabrication
Braun, et al., Nuclear Fusion, 63, 2022; Zylstra, et al., Phys. Plasmas, 2020 (Hybrid-B)

## Slide 27: Like asymmetry, more mixing (from capsule defects + hydro) costs energy, putting more demands upon the driver
Chart: Energy and Yield amplification "cost" of mix for N210808-like implosion
| 24.114890640000002 | 23.743421625000003 | 23.130714000000001 | 22.526015624999999 | 21.929326500000002 | 21.340646625000002 | 20.759976000000002 | 19.622662500000001 | 18.517386000000002 | 17.444146500000002 | 14.416650000000001
fB=1 | 48.8791 | 33.1991 | 15.4349 | 9.1306 | 6.4153 | 4.9738 | 4.0897 | 3.0645 | 2.4886 | 2.1206 | 1.541
fB=1.2 | 44.3351 | 16.0622 | 12.0906 | 8.8729 | 6.3606 | 3.9588
fB=1.4 | 37.5714 | 11.095 | 5.1571 | 3.6105 | 2.8552
No mix
Mix
More Mix
Energy “cost”
For ignition:
e-
Compressed
DT fuel with hot central core
Spitzer thermal conduction
Brems x-ray loss
Alpha-heating
Density
Temperature
DT mass ablation
in
in
Re-radiation
depends upon

## Slide 28: After years of effort, we got more energy from the NIF laser (1.9 MJ → 2.05 MJ) and had reasonable capsule quality, enabling the most recent success
Chart: DD Tion (keV)
| 2.8166523399999996 | 3.10177755 | 3.7102224349999999 | 1.9656060500000001 | 2.2562298599999999 | 2.3196550899999999 | 3.2306102800000001 | 3.0590000000000002 | 3.42 | 3.0874999999999999 | 2.698 | 3.1196316599999996 | 3.1825000000000001 | 1.482 | 2.4129999999999998 | 1.7694832999999999 | 2.16019797 | 2.6512360599999996 | 1.2961119799999998 | 1.4681817749999999 | 2.58324665 | 1.5718612599999999 | 1.52 | 1.9664999999999997 | 1.823855885 | 2.3198154500000001 | 2.0139999999999998 | 2.8982476500000001 | 2.3524722699999998
Lowfoot | 2.3007e+14 | 4.9853e+14 | 4.9268e+14 | 2.0131e+14 | 5.4208e+14 | 7.0044e+14 | 7.0125e+14 | 2.671e+14 | 6.6739e+14 | 8.9073e+14 | 3.7191e+14 | 718077391559984 | 6.6947e+14 | 114506738445614 | 417573826559862 | 1.5884e+14 | 2.7533e+14 | 5.3601e+14 | 1.5712e+14 | 1.3491e+14 | 5.3264e+14 | 9.9416e+13 | 1.1848e+14 | 2.962e+14 | 1.9182e+14 | 3.6208e+14 | 1.8334e+14 | 5.5419e+14 | 3.5005e+14
Highfoot | 8.6358e+14 | 6.3932e+14 | 1195303212552838 | 5.3786e+14 | 2.784e+15 | 5053722543452773 | 5959595564216789 | 3457388933441035 | 9247294435034856 | 3.213e+15 | 9212715514096852 | 6049984620508881 | 7112184639304813 | 9008657158494278 | 4946812097430978 | 6237640532699912 | 5471636750709320 | 3.5665e+15 | 3.2185e+15 | 7233783891383544 | 8670326219332719 | 5762823827312619 | 5533608524370136 | 6683306150932161 | 8095378221881889 | 6818474297884493 | 3087425113360610 | 5602244302685341 | 4.389e+15 | 6316168264117427 | 3313826289796072 | 10711842442947206 | 2803891516187706 | 4729047336431093
HDC | 5.3597e+14 | 1.7963e+15 | 1712664650695105 | 2.8645e+15 | 3.1245e+15 | 5238516636221929 | 2.1943e+15 | 7407405694437828 | 16488410188316704 | 9932156315524684 | 18827464044589872 | 17075549838955372 | 16941525813787744 | 11759705394782046 | 9176806260598032 | 11918661284430708 | 18098118121775908 | 15290284318391468 | 17529354646190830 | 11800628003475570 | 18828885893439072 | 10298114522134856 | 12988951744342700 | 11928164346638864
Bigfoot | 1.8565e+15 | 2.6028e+15 | 7490982936074811 | 10943626537285760 | 6233927031704696 | 7956920550468615 | 10268569444661902 | 11243077854423324 | 19571038072255672 | 10767125212399366 | 10157188017659130 | 13811493691834616 | 17217470464129840 | 7219011028228234 | 17331493555461886
HyE 1100 | 7487396477244934 | 19054577441139372 | 20273661169132376 | 5633721647119410 | 14444780994508152 | 6582032860372935 | 14306884129055594 | 6560353168367902 | 18092074881857056
HyE 1050 | 10165325251067788 | 34897198150358572 | 59994940952025360 | 51229341330607496 | 21993951417861648 | 12120065050731218 | 46431132611540376 | 4.7831e+17 | 1.5405e+17 | 2.4968e+17 | 1.7105e+17 | 89201152115301552 | 57709720915198552 | 4.09e+17 | 9.53e+17
Iraum | 6747266238726404 | 17825174083221002 | 17808213002747668 | 37685194612347104 | 56983885401791256 | 24132771452484060
Chart: Hot spot peak pressure (Gbar)
| 36.300390418507163 | 38.201815644096094 | 73.540545281612395 | 88.478314699521903 | 100.38498481154691 | 77.56558155614411 | 89.899370104105657 | 81.324287847115812 | 81.195003667948043 | 82.841709981997823 | 74.893791487041838 | 108.01484490028928 | 95.965986858869897 | 101.70938529975722 | 105.56478533690347 | 102.59436226562764 | 77.558365829556152 | 56.630182685752466 | 102.26762536234986 | 78.004036611990415 | 68.783167527125826 | 64.722289545101617 | 73.39828854496929 | 91.266462842672311
Lowfoot | 0.6497 | 1.4078 | 1.3913 | 0.56846 | 1.5308 | 1.978 | 1.9802 | 0.75427 | 1.8846 | 2.5153 | 1.0502 | 2.0278 | 1.8905 | 0.32335 | 1.1792 | 0.44856 | 0.77748 | 1.5136 | 0.44368 | 0.38096 | 1.5041 | 0.28074 | 0.33458 | 0.83642 | 0.54166 | 1.0225 | 0.51774 | 1.565 | 0.9885
Highfoot | 2.4387 | 1.8054 | 3.3754 | 1.5188 | 7.8617 | 14.2711 | 16.8292 | 9.7632 | 26.1132 | 9.0732 | 26.0156 | 17.0844 | 20.0839 | 25.4393 | 13.9692 | 17.6143 | 15.4512 | 10.0713 | 9.0885 | 20.4273 | 24.4839 | 16.2735 | 15.6262 | 18.8728 | 22.8604 | 19.2545 | 8.7185 | 15.8201 | 12.394 | 17.8361 | 9.3578 | 30.2489 | 7.9178 | 13.3543
HDC | 1.5135 | 5.0726 | 4.8364 | 8.0891 | 8.8232 | 14.7929 | 6.1965 | 20.9176 | 46.5613 | 28.0472 | 53.1665 | 48.2193 | 47.8408 | 33.208 | 25.9142 | 33.6568 | 51.1069 | 43.1779 | 49.5008 | 33.3235 | 53.1705 | 29.0806 | 36.6792 | 33.6837
Bigfoot | 5.2425 | 7.3501 | 21.1536 | 30.9035 | 17.6038 | 22.4694 | 28.9972 | 31.7491 | 55.2662 | 30.405 | 28.6827 | 39.002 | 48.62 | 20.3856 | 48.942
HyE 1100 | 21.1435 | 53.8078 | 57.2503 | 15.9089 | 40.7903 | 18.5869 | 40.4009 | 18.5256 | 51.0898
 | 28.7056 | 98.5454 | 169.4184 | 144.6654 | 62.1082 | 34.2256 | 131.1158 | 1350.7028 | 435.0173 | 705.0535 | 483.0196 | 251.8931 | 162.9652 | 1154.9659 | 2691.1553
Iraum | 19.0535 | 50.3361 | 50.2882 | 106.4184 | 160.9155 | 68.148
Pressure limited by explosion-phase
By addressing problems in steps and using a basic principles understanding, coupled with design optimization and finesse, went from 1.5 kJ to 3.15 MJ fusion yield

## Slide 29: HYBRID-E is the first ICF design to obtain a burning plasma1 and ignition2 in the laboratory
Key elements:
Up to 20% larger radius capsule than previous HDC ablator designs
Reduced LEH size, for better x-ray confinement3, with symmetry control via CBET4/pointing
Lower laser peak power, but an extended duration of peak power in order to reduce “coast time” duration5
All resulting in increased hotspot energy and pressure
1Zylstra, et al., Nature, (2022); Kritcher, et al., Nature Phys. (2022); 3Ralph, et al. ”Hohlraum Scans Project,” APS-DPP (2021); 4Kritcher, et al., PRE (2018); 5Hurricane, et al. PoP, (2017)
2Abu-Shawareb, et al (Indirect Drive ICF Collaboration), PRL, 2021; Kritcher, et al, PRE, 2021; Zylstra, et al, PRE, 2021

## Slide 30: 8% thicker ablator (mshell), with +8% more laser energy, and improved symmetry pushed the 1.37 MJ result to 3.15 MJ
Neutron Imaging System; Vologev, et al., RSI, (2014)
1.37 MJ
3.15 MJ
Time integrated neutron imaging

## Slide 31: Increasing laser energy and capsule thickness by +8%,while maintaining symmetry control, obtained Gtarget > 1 Dec. 5, 2022
N210808
N221204
Chart: 
| 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12
 | 635.3 | 118.2 | 62.1 | 42.6 | 32.9 | 27.2 | 23.5 | 20.9 | 18.9 | 17.5 | 16.3 | 15.4 | 14.7 | 14 | 13.5 | 13.1
 | 986.141 | 125.7 | 62.44 | 41.84 | 31.2 | 26.33 | 22.7 | 20.2 | 18.4 | 17 | 16 | 15.1 | 14.5 | 13.9 | 13.5
 | 571.9 | 107.7 | 56.4 | 38.5 | 29.8 | 24.7 | 21.5 | 19.2 | 17.6 | 16.4 | 15.4 | 14.65 | 14 | 13.5
 | 7.3472 | 6.4755 | 10.9208 | 13.6791 | 16.2522 | 11.3928 | 15.8479 | 13.7058 | 11.8852 | 12.8677 | 12.953 | 14.9642 | 13.587 | 14.2601 | 12.5395 | 13.2797 | 11.91 | 10.4766 | 18.2036 | 15.1718 | 10.7926 | 10.0426 | 12.7134 | 15.6978
 | 15.5438 | 10.8456 | 9.7561 | 9.3654 | 16.4839 | 19.6488 | 18.0338 | 16.5406 | 24.1214 | 18.1731 | 22.0994 | 17.9437 | 18.3731 | 26.2072 | 22.6297 | 15.8974 | 18.119 | 17.9344 | 24.3595 | 21.6662 | 21.0444 | 16.0986 | 21.6036 | 27.2726 | 20.4435 | 17.8994 | 17.8167 | 15.7865 | 21.8281 | 15.7463 | 34.0981 | 22.3777 | 21.3178
 | 9.2005 | 15.379 | 16.6048 | 20.3648 | 16.9882 | 17.7167 | 57.1941 | 48.7691 | 39.3944 | 47.0461 | 43.1012 | 33.1564 | 22.1387 | 34.3996 | 44.2429 | 31.3791 | 42.7256 | 26.065 | 38.8884 | 28.9474 | 24.231 | 30.2916
 | 18.5112 | 24.5018 | 36.5918 | 33.0038 | 31.9666 | 49.5749 | 47.2821 | 50.0795 | 34.5873 | 35.1734 | 25.9325 | 29.3225 | 40.3637 | 22.1218 | 31.1349
 | 18.4568 | 27.8191 | 23.008 | 12.847 | 24.8328 | 18.7196 | 16.8703 | 26.1874
 | 21.1963 | 33.0304 | 31.4557 | 36.8198 | 32.3022 | 30.7998 | 49.948 | 47.7636 | 42.051 | 44.46 | 49.59 | 29.328 | 43.659 | 46.62 | 48.6
 | 22.8841 | 24.3801 | 33.012 | 37.495 | 43.757
N210808
1.37 MJ
N221204
3.15 MJ
Lawson
ignition boundary
N220919
1.2 MJ
N211107
0.7 MJ
Delivered Laser Pulse
Lawson Metric Space
DD Tion (keV)
p𝝉 (atm-s)
Story of success by “incremental” evolutionary improvements

## Slide 32: Outstanding problem: materials appear stiffer than models expected and higher compression is needed for increased burn efficiency
Chart: In-flight adiabat
C | 14.4362 | 14.0166 | 16.6905 | 15.0028 | 16.5061 | 14.7377 | 15.8196 | 15.8683 | 15.648 | 14.5035 | 15.9443 | 16.0757 | 14.7849 | 17.0869 | 15.325 | 15.3802 | 14.6387 | 15.4007 | 14.1081 | 13.3042 | 15.0869 | 14.9239 | 16.7661 | 16.6374 | 16.5714 | 13.4577 | 14.5687 | 16.3686 | 15.2808 | 15.4348 | 15.2761 | 14.0072 | 15.3095 | 16.1058 | 16.3949 | 14.5036 | 15.2989 | 15.5853 | 16.4319 | 16.5833 | 17.0412 | 15.4059 | 15.8983 | 16.9362 | 16.2162 | 15.3197 | 15.2524 | 15.0453
C 3-2-Shock | 13.6473 | 17.7048 | 16.8204 | 15.0575 | 15.4549 | 15.176 | 16.255 | 14.3831 | 14.3288 | 14.0617 | 15.8433 | 15.5192 | 15.39 | 15.4368 | 14.8105 | 14.4074
Be | 18.1302 | 17.327 | 17.2283 | 19.1991 | 18.7175
Expected compressibility based on entropy
Measured compression
theory
Figure from: Landen, et al., PoP, 28, 042705 (2021)
Fraction of DT fuel burned:
Fraley, et al., Phys. Fluids, 17, 1974
The end of the beginning...there is more work to do!

## Slide 33: Remarkable that we can now talk about burning plasmas, ignition, and scientific breakeven (Gtarget > 1) in the past-tense!
No mystery physics obstacle stands in the way of ignition (explosive thermodynamic instability) or gain (energy out > energy in)
The theoretical prediction of the physics parameter regime (e.g. Lawson triple product) where ignition was expected consistent with our results
Additional laser energy (at fixed power) was very beneficial (”low coast time”)
Implosion physics was more sensitive to engineering control of the laser and targets than originally thought
So far, very high gain (high compression) target designs have not worked as expected. All break-throughs over the past decade have used low gain designs

## Slide 34
Disclaimer
This document was prepared as an account of work sponsored by an agency of the United States government. Neither the United States government nor Lawrence Livermore National Security, LLC, nor any of their employees makes any warranty, expressed or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States government or Lawrence Livermore National Security, LLC. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States government or Lawrence Livermore National Security, LLC, and shall not be used for advertising or product endorsement purposes.

## Slide 35: Coast-time slide