## Slide 1
Plasmas For Propulsion: Alternative Propellants And (Some) Emerging Concepts
Trevor Lafleur
University of New South Wales Canberra, Australia
MIPSE Seminar, Ann Arbor, 4 October 2023

## Slide 2: COLLABORATORS (1/2)
Lui Habl, Elena Zorzoli Rossi, Dmytro Rafalskyi
ThrustMe, France
Anne Bourdon, Pascal Chabert, Benjamin Esteves
Laboratoire de Physique des Plasmas, Ecole Polytechnique, France
Oliver Jia-Richards
Department of Aerospace Engineering, University of Michigan, USA
Javier Martinez Martinez
Independent, Germany

## Slide 3: COLLABORATORS (2/2)
Ash Pascale and Cormac Corr
Research School of Physics, Australian National University, Australia

## Slide 4: SEMINAR “SCOPE”
Plasma Propulsion
Generation of a force for moving a spacecraft
Plasmas play a critical role in the force generation or propulsion process

## Slide 5: SEMINAR OVERVIEW
1. Electrostatic propulsion
Challenges with conventional propellants and emerging alternatives
2. Inductive electrothermal propulsion
A novel propulsion technology for an identified market gap
3. Propellantless plasma propulsion
Utilization of the natural background plasma in the ionosphere

## Slide 6: 1. ELECTROSTATIC PROPULSION

## Slide 7: WHAT PROPELLANT SHOULD WE PICK?
Credit: Science Notes
Answer: It depends on the propulsion technology and mission…
Credit: NASA
Credit: NASA
SERT-1
NEXT

## Slide 8: EXAMPLE: GRIDDED ION THRUSTERS (GITS)
Thrust:
Power:
Thrust-to-power ratio:
Higher particle mass
Lower particle mass
Low voltage, high current thruster
High voltage, low current thruster
Smaller thruster size/mass*
Larger thruster size/mass
Answer (for GITs): Pick a convenient heavy propellant
*E. Stuhlinger, Ion propulsion for space flight (McGraw-Hill, 1964)

## Slide 9: XENON
Credit: Frank Stahl
Produced through fractional distillation of air
Low concentration (1 part per 11.5 million) but not “rare”
For every 1000 tons of O2 produced, only 1.2 kg of Xe are collected
Cost can be as high as $3000/kg
D.A. Herman and K.G. Unfried, “Xenon acquisition strategies for high-power electric propulsion NASA missions”, JANAF SPS Subcommittee Meeting, GRC-E-DAA-TN23198
Challenge: Xe is expensive
Challenge: The Xe market is susceptible to strong fluctuations
Short-term solution: Adopt Kr and Ar as alternatives?

## Slide 10: SPACE INDUSTRY GROWTH
Between 17,000 – 300,000 satellites could be launched over the next 10 years with an average satellite mass of ~300 kg
”Satellites to be built and launched by 2029”, market research report, Euroconsult, 2021
“Global satellite manufacturing and launch market”, market research report, Northen Sky Research, 2022
A. Lawrence et al, “The case for space environmentalism”, Nature Astronomy 6, 428 (2022)
Chart: 
| 100 - 500 kg | 1 - 100 kg | > 500 kg
Column1 | 77.5 | 16.77 | 5.73
77.5% (100 – 500 kg)
5.7% (> 500 kg)
16.8% (1 –100 kg)
Satellite Mass Distribution
Challenge: Global Xe production is only ~60 metric tons/year
2000 satellites/year
x 30 kg of propellant
= 60 metric tons/year

## Slide 11: IODINE AS AN ALTERNATIVE PROPELLANT
Extracted from caliche ore or underground brines
Global iodine production estimated to be almost 30,000 metric tons (500x higher than Xe)
Cost can be as low as $50-$100/kg (50-100x cheaper than Xe)
Credit: Ajay-SQM Group
Credit: Iochem
K. Hora, “Iodine production and industrial applications”, IDD Newsletter, 2016
*V.G. Tirila et al, “Review of alternative propellants in Hall thrusters”, 2Acta Astronautica 212, 284 (2023)
Advantage: Low cost
Advantage: High global production output
Advantage: Easy handling and transport
*Other alternatives: Zn, Bi, Mg?

## Slide 12: STORAGE DENSITY
Advantage: I2 needs a smaller tank
Xe
Kr
I2
Ar
Relative Storage Tank Size (200 atm, 20 oC)
x1
x2.3
x5
x14
NIST Chemistry WebBook, 2023
Advantage: I2 needs a lighter tank

## Slide 13: IODINE FLOW CONTROL
~114 oC
Challenge: Solid iodine flow control
I2(s)
I2(g)
Thermal control system (heater, temperature sensor, control algorithm)
Solution: Controlled sublimation
NIST Chemistry WebBook, 2023
D. Rafalskyi et al, “In-orbit demonstration of an iodine electric propulsion system”, Nature 599, 411 (2021)

## Slide 14: IODINE PROPULSION “TIMELINE”
2019
First in-space demonstration of an iodine propulsion system (cold/warm gas thruster; ThrustMe)
2012
First(?) ground-based demonstration of an iodine-fueled electric propulsion system (Hall thruster; Busek)
2000
Recognition of cost/availability problems of xenon in the future and the proposal of iodine as a primary propellant
1962
Investigation of negative iodine ions as an alternative to electrons for neutralization
2020
First in-space demonstration of an iodine electric propulsion system (gridded ion thruster; ThrustMe)
2021-
Further launches of iodine electric propulsion systems (ThrustMe, T4i, Busek)
W. Dong et al, “Negative iodine formation on metal hexaboride surfaces”, ARS Electric Propulsion Conference, 1962
R. Dressler, Y.-H. Chiu, and D. Levandier, “Propellant alternatives for ion and Hall effect thrusters”, 38th Aerospace Sciences Meeting and Exhibit, AIAA-2000-0602, 2000
O. Tverdokhlebov and A. Semenkin, “Iodine propellant for electric propulsion-to be or not to be”, 37th Joint Propulsion Conference and Exhibit, AIAA-2001-3350, 2001
J. Szabo et al, “Performance evaluation of an iodine-vapor Hall thrusters”, Journal of Propulsion and Power 28, 848 (2012)
J. Martinez Martinez, D. Rafalskyi, E. Zorzoli Rossi, and A. Aanesland, “Development, qualification and first flight data of the iodine based cold gas thruster for CubeSats”, 5th IAA Conference on University Satellite Missions and CubeSat Workshop, 2020
D. Rafalskyi et al, “In-orbit demonstration of an iodine electric propulsion system”, Nature 599, 411 (2021)

## Slide 15: FIRST IN-ORBIT DEMONSTRATION
ThrustMe NPT30-I2 first launched into space on 6 November 2020 onboard the Beihangkongshi-1 satellite
480 km circular Sun-synchronous orbit
In-space testing between 2020-2021 with first ignition 29 December 2020
D. Rafalskyi et al, “In-orbit demonstration of an iodine electric propulsion system”, Nature 599, 411 (2021)

## Slide 16: THRUST AUDIT
Thrust audit of the ThrustMe NPT30-I2 propulsion system
O. Jia-Richards and T. Lafleur, “Iodine electric propulsion system thrust validation: from numerical modelling to in-space testing”, Journal of Propulsion and Power, articles in advance, 2023
Credit: ThrustMe

## Slide 17: OTHER IODINE PROPULSION SYSTEMS
Gridded Ion Thruster (ThrustMe)
Hall Thruster (Busek)
Ambipolar Thruster (T4i)
Gridded Ion Thruster (Busek)
Cold/Warm Gas Thruster (ThrustMe)
RF Neutralizer (Busek)

## Slide 18: IODINE PLASMA CHEMISTRY
Xenon (Xe)
Atomic Iodine (I)
Molecular Iodine (I2)
H.B. Ambalampitiya et al, “Electron scattering cross-section calculations for atomic and molecular iodine”, Atoms 9, 103 (2021)
J.R. Hamilton and J. Tennyson, “Iodine: I2 molecular and I atom”, technical report, Quantemol, 2015
T. Lafleur et al, “Development and validation of an iodine plasma model for gridded ion thrusters”, Plasma Sources Sci. Technol. 31, 114001 (2022)

## Slide 19: EXCITATION REACTIONS
Xenon (Xe) | 
Configuration | Energy (eV)
5p6 | 0.00
5p5(2Po3/2)6s | 8.32
5p5(2Po3/2)6s | 8.44
5p5(2Po1/2)6s | 9.45
5p5(2Po1/2)6s | 9.57
Atomic Iodine (I) | 
Configuration | Energy (eV)
5s25p5 | 0.00
5s25p5 | 0.94
5s25p4(3P2)6s | 6.77
5s25p4(3P0)6s | 6.95
5s25p4(3P1)6s | 7.55
NIST Atomic Spectra Database, 2023
T. Lafleur et al, “Development and validation of an iodine plasma model for gridded ion thrusters”, Plasma Sources Sci. Technol. 31, 114001 (2022)
B. Esteves, “Investigation of iodine plasmas for space propulsion applications”, PhD thesis, Ecole Polytechnique, 2022
K. Holste et al, “Performance of an iodine-fueled radio-frequency ion-thruster”, Eur. Phys. J. D 72, 1 (2018)
Advantage: Collisional energy loss is lower in iodine (Te > ~4 eV)

## Slide 20: PLASMA MODELLING (1/3)
Iodine | I2, I, I2+, I+, I2+, I-, e-
Continuity equation for each species:
Global electron power balance:
Electromagnetic ICP model:
Global neutral gas heating equation:
Ground state (and some excited states)
P. Grondein et al, “Global model of an iodine gridded plasma thruster”, Phys. Plasmas 23, 033514 (2016)
T. Lafleur et al, “Development and validation of an iodine plasma model for gridded ion thrusters”, Plasma Sources Sci. Technol. 31, 114001 (2022)
B. Esteves, “Investigation of iodine plasmas for space propulsion applications”, PhD thesis, Ecole Polytechnique, 2022
D. Levko and L.L. Raja, “Fluid modelling of inductively coupled iodine plasma for electric propulsion conditions”, J. App. Phys. 130, 173302 (2021)
S. Andrews et al, “Coupled global and PIC modelling of the REGULUS cathode-less plasma thrusters operating on xenon, iodine and krypton”, Acta Astronautica 207, 227 (2023)

## Slide 21: PLASMA MODELLING (2/3)
T. Lafleur et al, “Development and validation of an iodine plasma model for gridded ion thrusters”, Plasma Sources Sci. Technol. 31, 114001 (2022)
Credit: ThrustMe

## Slide 22: PLASMA MODELLING (3/3)
Current iodine reaction set seems quite good!
Credit: ThrustMe
38 mg/s
58 mg/s
99 mg/s

## Slide 23: IODINE MATERIAL COMPATIBILITY
J. Martinez Martinez and D. Rafalskyi, “Design and development of iodine flow control systems for miniaturized propulsion systems”, CEAS Space Journal 14, 91 (2022)
D. Zschatzsch et al, “Corrosion of metal parts on satellites by iodine exposure in space”, Journal of Electric Propulsion 1, 1 (2022).
Challenge: Iodine is reactive with many materials!
High Chemical Reactance With Iodine
Aluminium and aluminium alloys
Stainless steel and stainless-steel alloys
Copper
Tin
Low Chemical Reactance With Iodine
Refractory metals
Technical ceramics
Polymers and polymer coatings
Al 6082 SEM micrography
Solution: Careful material selection

## Slide 24: 2. INDUCTIVE ELECTROTHERMAL PROPULSION

## Slide 25: PROPULSION COMPARISON
Thrust (“Maneuver Time”)
Specific Impulse (“Fuel Efficiency”)
Cold Gas
Chemical Propulsion
Resistojet
Hall Thruster
Gridded Ion Thruster
Electrothermal Propulsion
Ambipolar Thruster
RF ICP Plasma “Torch”
Target
F/P = 100-200 mN/kW
Isp = 300-1000 s

## Slide 26: ELECTROTHERMAL THRUSTERS
DC discharge
Immersed electrodes
Flight heritage
Microwave discharge
No immersed electrodes
Resonant cavity device
Limited flight heritage
RF discharge
No immersed electrodes
Non-resonant device
No flight heritage
Significant heritage in the plasma torch community
Y. Shen et al., Chin. Journal Aeronaut. 33, 3011 (2020)
M.M. Micci, S.G. Bilén and D.E. Clemens, Prog. Propul. Phys. 1, 425 (2009)
T. Fujino and M. Yamauchi, J. Appl. Phys. 128, 173302 (2020)
M.M. Micci, Encyclopedia of Aerospace Engineering (Wiley, 2010)
Arcjet
Microwave (MET)
RF ICP

## Slide 27: INDUCTIVELY COUPLED PLASMAS (ICPs)
Advanced Manufacturing
Credit: Tekna
High-Enthalpy Flows and Aerothermodynamics
Credit: von Karman Institute
Analytical Chemistry
Credit: University of Toronto
Heat Losses

## Slide 28: THE BIDIRECTIONAL VORTEX
Credit: ORBITEC
G. Sharma and J. Majdalani, Phys. Fluids 33, 093607 (2021)
A.B. Vyas, J. Majdalani, and M.J. Chiaverini, “The bidirectional vortex. Part 1: An exact inviscid solution”, 39th AIAA/ASME/SAE/ASEE Joint Propulsion Conference and Exhibit, AIAA 2003-5052

## Slide 29: POWER TRANSFER PROCESS
RF Power
Enthalpy Flow
Ionization
Plasma-Wall Losses
Excitation, etc.
Circuit Losses
Gas-Wall Heat Losses
Nozzle Losses
Power Coupled to Plasma
Power Transferred to Gas
Power Leaving ICP

## Slide 30: EXPERIMENTAL SETUP
T. Lafleur and C. Corr, “Characterization of a radio-frequency inductively coupled electrothermal plasma thruster”, J. Appl. Phys. 130, 043304 (2021)

## Slide 31: OPTICAL EMISSION SPECTROSCOPY
Boltzmann Plot Method
Rovibronic N2 Bands
Peak Gas Temperature (K) | 10,000
Electron Density (m-3) | 1020 - 1021

## Slide 32: RF POWER TRANSFER EFFICIENCY

## Slide 33: WATER CALORIMETRY

## Slide 34: PERFORMANCE METRICS

## Slide 35: ISENTROPIC NOZZLE THEORY
Credit: Everyday Astronaut
Thrust coefficient:
Characteristic velocity:
A nozzle converts thermal/internal energy into directed energy:
Maximize Tc
Minimize M
Minimize g

## Slide 36: WHAT IS THE BEST PROPELLANT TO USE?
Conventional specific impulse:
Effective specific impulse:
Considers the entire propulsion system mass and propellant storage state
J. Martinez Martinez and T. Lafleur, “On the selection of propellants for cold/warm gas propulsion systems”, Acta Astronautica 212, 54 (2023)

## Slide 37: 3. PROPELLANTLESS PLASMA PROPULSION

## Slide 38: THE LEO SPACE ENVIRONMENT
Atmospheric drag:
Solar radiation pressure:
Ionospheric drag:
Electron temperature (K) | 1000 - 3000
Average Ion Mass (umu) | 5 - 20
R. Jastrow and C. Pearse, “Atmospheric drag on the satellite”, Journal of Geophysical Research 62, 413 (1957)
Mass Spectrometer and Incoherent Scatter radar (MSIS; 2000 version)
International Reference Ionosphere (IRI; 2016 version)

## Slide 39: SPACECRAFT POTENTIAL
Charged Hazards and Wake Studies (CHAWS): -5000 V
Credit: NASA
STPSat-3: -35 V to -25 V
Credit: Ball Aerospace
Upper Atmosphere Research Satellite (UARS): -90 V
Credit: NASA

## Slide 40: TOY MODEL
Energy conservation:
Angular momentum conservation:
Intercepted momentum flow:

## Slide 41: IONOSPHERIC DRAG MODEL
Method 1: Numerical Trajectory Calculation
Method 2: Analytical Solution
Effective (spherical) potential:
Drag force:
Direct collection
Deflection
T. Lafleur, “Charged aerodynamics: Ionospheric plasma drag on objects in low-Earth-orbit”, Acta Astronautica 212, 370 (2023)

## Slide 42: ION TRAJECTORIES

## Slide 43: DRAG FORCES
J. Praks et al, “Aalto-1 – An experimental nanosatellite for hyperspectral remote sensing”, 2011 IEEE International Geoscience and Remote Sensing Symposium, Vancouver, Canada, 24-29 July 2011.
C. Capon et al, “Numerical predictions for on-orbit ionospheric aerodynamics torque experiment”, IEEE Aerospace Conference, 2020.

## Slide 44: SUMMARY
Iodine as a propellant
Emerging alternative to xenon with attractive physical and plasma properties that has been successfully demonstrated in space
RF ICP electrothermal plasma thruster
Promising propulsion technology to meet industry needs and with the potential to use a wide range of conventional and non-conventional propellants (including reactive substances)
Propellantless plasma propulsion
Active spacecraft biasing can be used as a “solid-state” and propellantless mechanism for formation flying, deorbiting, collision avoidance, and attitude control

## Slide 45: PHD PROJECT AVAILABLE!
Topic: “Plasma CFD” simulations of vortex-enhanced supersonic inductively coupled plasmas
Collaborators: Research School of Physics at ANU and the von Karman Institute (VKI) for Fluid Dynamics in Belgium
Candidate profile: Strong mathematical, programming (C++, Python, and Linux ideally), and communication skills
Get to visit VKI in Belgium for several months as part of your PhD!
Credit: VKI