## Slide 1
Florida State University
Founded 1851, Enrollment 44,000
Ranked 18 of US Public Research Universities (USNWR)
Florida A & M University
Founded 1887, Enrollment 10,000
Public HBCU in Florida
FAMU-FSU College of Engineering
Founded 1982
Shared by FSU and FAMU
Chemical and Biomedical Engineering
Enrollment: 500 undergraduates, 50 graduates
18 tenure track faculty members
National High Magnetic Field Lab

## Slide 2: General Department Research Areas - Department of Chemical and Biomedical Engineering -
Biomedical Engineering
  Imaging (NMR,MRI) - Grant, Li, Holmes, Mohammadigoushki
  Cellular and Tissue Engineering – Grant, Li, Holmes
  Biomaterials - Ali, Guan, Holmes, Ramakrishnan
Materials
  Polymers - Alamo, Arnett, Chung, Hallinan, Ricarte
  Complex Fluids - Mohammadigoushki, Ramakrishnan
  Electronic Materials - Siegrist
  Nano - Materials – Ali, Grant, Guan, Hallinan, Kalu, Ramakrishnan, Siegrist
Chemical Engineering
  Catalysis – Chung
  Chemical Reaction Engineering – Locke
  Energy storage – batteries – Hallinan, Kalu

## Slide 3
Professor Bruce R. Locke
Hydroxyl Radicals in Gas-Liquid Water Plasma Reactors
Florida State University
Department of Chemical and Biomedical Engineering
Tallahassee, FL
Funding
National Science Foundation CBET – 1236225, 1702166
Czech Fulbright Commission, Florida State University

## Slide 4
Contacting Plasma with Liquid Water
Electrical discharge underwater (pulsed, RF, microwave)
- 10-3 to 1 J/pulse (also ns to ms pulses possible)
- up to kJ/pulse - electrohydraulic discharge,
arc formation, exploding wire
- breakdown underwater: 1 MV/cm
Underwater
Combined gas/liquid
Water spray
(AC, DC, or pulsed)
Gas-liquid Interface
Gliding arc
Bubbles
Films
Discharge in gas
- plasma in gas
- gas phase breakdown
- plasma touches water
surface
- liquid properties can
be important (conductivity)
Planar
Scaled prototypes
Notes: Examples from our work – not meant to be exhaustive – there are other methods as well, diaphragm discharge etc.

## Slide 5: Applications of Plasma with Liquid Water
Water pollution treatment
  Wide range of organic and some inorganic compounds – emerging contaminants – perfluorinated species, antibiotics, personal care products
Air pollution treatment (wet plasma – water sprays and films)
  Nitrogen and sulfur oxides, volatile organic compounds (VOCs)
Disinfection and biomedical
  Bacteria, yeast, viruses
  Biomedical – wound healing, cancer treatment
Chemical synthesis
  Partial oxidation – alcohols, aldehydes…
  Nanoparticle synthesis
  Polymer coatings
  Plasma activated water for agriculture uses – nitrates/nitrites, seed germination…
Many reviews on this subject published in last 10 years: Akiyama, Malik, Locke, Sunka,
Sato, Bruggeman, Lukes, Thagard, Weltmann, Brandenburg,…..
P. Bruggeman, M.J. Kushner, B.R. Locke, et al., Plasma-Liquid Interactions:
A Review and Roadmap, Plasma Sources Science and Technology, 2016
Notes: Recent review of the fundamental aspects of this topic will be published based upon the Lorentz Workshop held in Leiden Netherlands summer of 2014.

## Slide 6: Complexities of Gas-Liquid Water Plasma Chemistry
P. Bruggeman, M.J. Kushner, B.R. Locke, et al., Plasma Sources Science and Technology, 2016
(With air or argon)
Chemistry strongly dependent on gas composition (air, N2, O2, Ar, He)
Not all factors equally important or occur in all types of gas-liquid plasma
Notes: Gas –liquid plasma and the interactions of plasma at the surface of a liquid can be quite complex
Here we are not dealing with underwater discharges per se – have published extensively on that subject in previous work.

## Slide 7: Key Chemical Species from Electrical Discharge with Water
H2O +e-  H + ·OH + e-
Possible Products and active species
Molecules: (stable)
H2, O2, H2O2, (O3)
Radicals and atoms: (short life)
O, ·H, ·OH, HO2
Ions:
H+(H3O+), O+
H-, O-, O2·-, OH-
eaq-
Electron dissociation
•OH = 2.80 V
O = 2.42 V
O3 = 2.07 V
H2O2 = 1.77 V
•HO2 = 1.7 V
Standard oxidation potentials
H2O + M  H + ·OH + M
Thermal dissociation
Disinfection, chemical destruction
Stable molecular carrier for OH radicals
May be important for reduction reactions
Notes: Key species – simplified with oxygen and hydrogen only – not air.

## Slide 8: Hydroxyl Radical Generation from Water
Thermodynamic limit
(from DHr)
H2O  ∙OH + ∙H
H2O + e-  ∙OH + ∙H + e-
H2O + hn  ∙OH + ∙H
H2O + e-  ∙OH + ∙H + e-
20
(120 to 190 nm, depends on quantum yields and lamp efficiencies)
2 to 4 (in liquid)
7 to 9 (in gas with vapor)
(electron beams, gamma radiation)
Yields* (molecules/100 eV)
2 to 3 (in liquid)
5 to 6 (in gas with vapor)
* -note: yields estimated from literature where data was obtained under wide range of different operating conditions and measurement methods
Subject of this talk
UV light
Radiation
Plasma
Notes: What is the hydroxyl radical – electrically neutral, unpaired electron, when discovered etc. (throughout consider differences between gas and liquid phase reactions)
Why is the hydroxyl radical important – reaction rate constant – diffusion limits in gases and liquids – kinetics - fast rates lead to mass transfer limits
Where is the hydroxyl radical important – atmospheric chemistry, cellular biology, combustion, extraterrestrial space
How do you make hydroxyl radicals – thermal, photo, electrical, radiative – homogeneous vs heterogenous sources
What are the limitations on energy yields for hydroxyl radicals and therefore their reactions with targets?
How do you efficiency utilize hydroxyl radicals – since rate so fast can lose quickly, competing reactions
How to measure hydroxyl radicals – chemical, physical-optical-laser etc.
Role of hydroxyl radicals in plasma contacting liquid water
- other competing reactions and processes - complications
- comparison to radiation processes
- oxidation/reduction processes – oxidation vs reduction – should they balance in plasma?
- OH reactions in the liquid phase
- OH reactions in the gas phase

## Slide 9: Note on Importance of Hydroxyl Radical - Gas Phase -
Provides insight into oxygen and water chemistry in intersteller space: 104-106 cm-3 (low temperature and density)
Earth atmosphere:
  Formed in stratosphere by UV: 106 cm-3
  Cleans nitrogen oxides, organics from troposphere, 0.01 to 1 s
Indoor air – similar chemistry as in atmosphere
  Clean air: 104 to 105 cm-3
  Photolysis of HONO: 106 cm-3
  With air cleaners: 107 to 108 cm-3
Combustion – main reactant: 1014 to 1016 cm-3, high temperature and pressure (1 to 5% of species)
Gas phase plasma reactors (with water vapor):1013-1015 cm-3, atmospheric pressure and temperature
Notes: 1 – OH first observed in interstellar space by Weinreb in 1966

## Slide 10: Note on Importance of Hydroxyl Radical - Liquid Phase -
Close coupling of ∙OH with H2O2 in the liquid phase
Natural water:
  UV photolysis of nitrate, dissolved organic matter
    H2O2: 50-1000 nM
  Natural seawater – ∙OH: 10-9 to 10-6 nM
  Acid mine water – ∙OH: 10-5 to 10-3 nM
Found in biology
  Cells: H2O2 1 to 10 nM
Advanced oxidation technologies (∙OH based processes)
  O3, O3/H2O2, O3/H2O2/UV, Fenton(H2O2/Fe)
  ∙OH: 10-4 to 10-1 nM (quasi steady-state due to very high reactivity)
Plasma contacting liquid water
  ∙OH: 10-1 nM (quasi steady-state due to very high reactivity)
Notes: Difficult to measure OH in liquid

## Slide 11: Reaction Rate Constants (Second order M-1s-1, Tarr (2003))
 | ·OH | O3 | pH | eaq- | ·H
Benzene | 7.8x109 | 2 | 2-3 | 9.0x106 | 9.1x108
Phenol | 6.6x109 | 1300 2x106 | 2 7 | 2.0x107 | 1.7x109
Chloro-phenol | 12x109 | 1600 | 2 |  | 
Formic acid | 0.13x109 | 5 | 2-4 |  | 
Trichloro-ethylene | 4x109 | 17 | 2 | 1.9x109 | 
·OH reactions near diffusion limits 1010 M-1s-1 in liquids
Competing (reduction) reactions with ·H and eaq- (depends upon species)
O3 can be important if [O3]>>[·OH] (ozone solubility range 10-5 to 10-3 M)
  Rate(·OH)/Rate(O3) = 1 (chlorophenol); = 100 (others) (for max O3)
Notes: Rate = k (OH)(organic) = 1 s-1 (organic) (OH 10-1 M)
Rate = k (O3)(organic) = 0.01 s-1 (organic) for ozone = 0.001 M k =10 – ozone solubility 1 to 100 mg/l

## Slide 12: Idealized Reaction Pathways (with H2O only)
H2O  H∙ + ∙OH
(Primary yield -
radiation chemistry)
Molecular products
(stable)
H2, O2, H2O2
(Ideal quenching - Fridman)
∙OH + organic  products
Desired reactions in/near plasma
(very fast reactions)
∙OH quenching…
H∙ + ∙OH  H2O
(Absolute quenching - Fridman)
∙OH + H2O2  prods

Undesired reactions in/near plasma
Used outside of plasma
H2O2 – in liquid
H2 and O2 – in gas
∙OH + ∙OH H2O2
∙H + ∙H H2
…. O2
Notes: Primary yield – concept from radiation chemistry, accessible with chemical probes to stop reactions to other products…

## Slide 13: Underwater Discharge
Discharge Reactions
H2O +e-  ·H + ·OH + e-
H2O + M  ·H + ·OH + M
Recombination Reactions
·OH + ·OH  H2O2
·O + ·O  O2
·H + ·H  H2
·H + O2  HO2∙
HO2∙ O2∙- + H+
Overall (Bulk) Reaction
(Experimental Observations)
6H2O  4H2 + 2H2O2 + O2
(Mededovic and Locke, 2008, 2009, 2012)
(Joshi et al. 1995; Grymonpre et al. 1998, 1999, 2001;
Kirkpatrick and Locke, 2005)
Water
level
HV
High T core
Cooler recombination zone
Notes: We also measured OH and total reducing species.

## Slide 14: Comments from Radiation Chemistry (Buxton, 1987; Magee and Chatterjee, 1987)
Geometrical patterns of energy deposition from high energy electrons
Chemical probes used to determine primary yields – products formed in the chemical core
Note: O and O2 not typically found in underwater radiation reactions
Non-homogeneous energy deposition, fast time scales
Kinetics in spur leads to homogeneous kinetics at 10-7 s
Primary Products
Radiation track structure

## Slide 15
Bubbles
H2Oliq
Vapor
bubble
electrode
1 cm
Planar Surface
H2Oliq
Gas phase
electrode
5 cm
electrode
H2Oliq
Gas flow
Water film reactor
4 mm
Discharges at Gas-Liquid Interface
Plasma propagates in gas phase along the gas/liquid interface
Requires lower electric field to generate plasma than inside water
More efficient generation of plasma
Flow direction
Batch, semi-batch systems
Continuous flow system
(Shih and Locke, 2009)
(Wandell and Locke, 2014)
(Grymonpre et al., 2004)
Flow system useful to control gas, liquid, and plasma contacting, fluid residence times, and to measure gas and liquid products and reactants.
Notes: Here are a few of the many ways to generate plasma at the interface with liquid water.
focus on the continuous flow small reactor since we can control the gas and liquids (semi-independently) and can focus on a small section of the plasma at the gas-liquid interface.
Show where electrodes are placed.

## Slide 16
Flowing Film Plasma Reactor System
Eagle Harbor
Nanopulser
Gases
Gas samples:
FTIR (on-line)
GC, GC/MS,
NMR
Liquid samples:
GC, GC/MS, NMR,
UV spectroscopy
Optical emissions
Spectrometer
(w/ optical fiber)
Notes: Small reactor – control input conditions, measure output products, in situ plasma diagnostics. Nanopulser power supply Eagle Harbor
Shows one of two different power supplies used.

## Slide 17
High Speed Imaging
Gas flow region
Liquid film flow region
4 mm
3 mm
Gas-liquid interface / Plasma discharge region
*4,000 fps
Flow direction
*1/12,000 sec. shutter speed
*1/60 sec. shutter speed
Deionzed water with argon carrier.
Notes: Images show liquid flow characteristics and plasma channel propagation.
Plasma propagates along the interface between the gas and liquid. Plasma covers surface with multiple pulses – single channel per pulse. These are with the ignition coil power supply (next).

## Slide 18
Input waveform properties
Peak voltage
Frequency
Pulse width and shape
Rise time
Discharge waveform properties
Breakdown voltage
Peak current
Total current
Energy per pulse
Plasma properties
Plasma gas temperature
Electron density
Electron energy (distribution)
Size (diameter, volume) plasma channel
Chemical species formation
∙OH, H2O2, etc. - reaction and production rates
∙OH, H2O2, etc. - energy yield
Reactor configuration
Electrode gap distance
Nozzle size
Reactor volume, shape
Liquid flow rate
Gas flow rate
Transport Processes
Hydrodynamics
  Gas volume
  Liquid volume
  Residence times, mixing patterns
Mass and energy transport processes
Feed species
Gas composition
Liquid composition
  pH, conductivity
Connecting Physical and Chemical Processes

## Slide 19: Reactor Characterization
Geometrical Properties (Wandell et al., 2018)
  Volumes of liquids and gases
  Interfacial area (gas-liquid and plasma-liquid)
  Residence times of liquids and gases
    100-250 ms (liquid), 2–5 ms (gas); nozzle size dependent
Hydrodynamics (Wandell et al., 2018)
  Roles of nozzle size, gas and liquid flows
  Flow patterns and regimes (annular flow)
  Pressure in reactor (choked flow) higher pressure forces liquid to form film on walls
  No evidence of plasma discharge affecting hydrodynamics
Mass and energy transfer (Hsieh et al., 2016)
  Liquid and gas (film theory)
  Liquid and plasma
Notes: Geometrical properties affect flow and transport.
Residence time has strong affect on chemical reactions. Today only discuss some aspects of mass transfer at the interface, which make this reactor advantageous.

## Slide 20: Electrical and Plasma Properties
Waveforms
  Ignition coil (microsecond pulser)
  Nanopulsers
Plasma properties
  Plasma gas temperature
  Electron density
  Electron energy
  Plasma volume
Effects of reactor conditions (Wang et al. 2018, 2019)
  Effects of carrier gas composition
  Effects of gas and liquid flows
  Effect of pulse properties
  Effects of solution conductivity

## Slide 21: Power Supplies - Nanopulsers
2) Eagle Harbor Technologies (commercial)
2 kHz, 5.5 kV peak, 20 ns (rise), 0.3 kV/ns,
150 mJ/pulse, 0.30 W, argon
voltage
current
power
Frequency range: to 10 kHz
Pulse width range: 20 to 260 ns
1) Airity Technologies (custom)
1 kHz, 3.8 kV peak, 140 ns (rise)
130 mJ/pulse, 0.13 W, argon
current
voltage
power
Energy: 80 to 140 mJ/pulse
Frequency Ranges: to > 60 kHz

## Slide 22: Power Supplies – Microsecond Pulsers
3) Ignition Coil Based (Professor Radu Burlica – Iasi, Romania)
High efficiency ignition coil
  Audi
DC power supply
  input voltage (12 V)
  BK Precision 1740B
Frequency generator
  500 Hz, 40% duty cycle
  BK Precision 4010A
Characteristics:
  Inexpensive, small
  Microsecond pulses
  Robust
  Limited control, Waveforms noisy
  Restricted range of liquid
  conductivities (500 mS/cm)
500 Hz pulse, argon
with deionized water
Yellow = voltage
Red = power
Blue = current (~ 200 ms)
(200 ms)
Notes: Comments – other power supplies under investigation including the power supply in Prague and a custom made nanopulser from California (Airity)
Nano-pulser – for lab can be expensive

## Slide 23: Temperature Measurement Methods
Trace N2 added
N2 (C-B)
Specair fitting
Two temperature fitting Boltzmann plot of OH (A-X)
Program from Dr. Jan Vorec (Masaryk University)
Example: (Eagle Harbor nanopulser)
  Power setting: 12kV 20ns 2kHz
  Water flow rate: 2 ml/min
  Helium
(Wang, Wandell, Locke, 2018)
Notes: Two methods – N2 and OH

## Slide 24: Plasma Gas Temperature Results (Eagle Harbor nanopulser)
Method of measurement, N2 or OH, gives similar results.
Helium significantly cooler than argon.
Temperature independent of discharge power.
(Wang, Wandell, Locke, 2018)

## Slide 25: Electron Density Measurement (Eagle Harbor nanopulser)
Ha fitting: example, 18 kV, 20 ns, 2 kHz
Argon
Helium
(Wang, Wandell, Locke, 2018)

## Slide 26: Electron Density Results (Eagle Harbor nanopulser)
Chart: Discharge power (Watts)
| 0.29433333333333334 | 0.4957333333333333 | 0.65533333333333332 | 0.97953333333333326
Ar | 18413530962557700 | 19372274395202536 | 19813412103619656 | 20231407599703024
He | 1278920029948190 | 1.8866e+15 | 2020482482225634 | 2273366994452750
(Wang, Wandell, Locke, 2018)
Electron density in helium 1 order of magnitude lower than in argon.
Electron density in helium relatively more sensitive to discharge power.
Discharge power varied by changing voltage.

## Slide 27: Time Resolved Electron Density (Eagle Harbor nanopulser)
(20 kV, 1 kHz, and 20ns, DI water liquid flow rate 2 mL/min)
(Wang, PhD dissertation, 2018)
Time (ns)
Wavelength (nm)
Note time decay of electron density longer than current/voltage pulse in argon.
(argon)

## Slide 28: Influence of Liquid Conductivity (Eagle Harbor nanopulser)
Argon
Helium
Plasma properties relatively unaffected by large changes in liquid conductivity.
(Discharges effectively in near seawater, (seawater = 50 mS/cm), conductivity.)
Unique for EH nano-pulser (not found with microsecond pulser), fast rise time.
Some effects of conductivity above 36 mS/cm seen for argon, but not helium.
(Wang et al., 2019)

## Slide 29: Chemical Processes Analyzed - role of hydroxyl radicals -
A simple model of hydroxyl radical formation (Wang et al., 2018)
Hydroxyl radical formation from probes (ignition coil, nanopulser)
  Methylene Blue (non-volatile, liquid phase) (Hsieh et al., 2016)
  Ethanol probe (volatile, liquid phase) (Hsieh et al., 2017)
  Carbon dioxide probe (gas phase) (Hsieh et al., 2017)
  Effect of frequency (EH and Airity nanopulsers)
Hydrogen peroxide formation (EH nanopulser)
  Effects of flow and carrier gas (Wang et al., 2018a)
  Effects of solution conductivity (Wang et al., 2018b)
  Effect of pulse properties (Wandell et al., 2018)
Hydrocarbon partial oxidation (Bresch et al., 2015, PCPP)
Dioxane oxidation with plasma + bioreactor (Yiong et al., 2019)
Nitrogen oxide formation (Wandell et al., 2019; Bulusu et al. 2019)
  Hydroxyl radicals with gas phase probes (NO and CO)
  Gas phase NO/NO2 measurements, liquid phase NO2-, NO3-

## Slide 30: Reaction Model Based upon Fast Quenching in Film
Hydrogen peroxide mass balance in film: neglect diffusion and spatial variation in film
Decreasing with pulse
Production Rate
Plasma core
Plasma film
l=(2Ditp)1/2
= 1 mm
Cross section of plasma channel
Notes: All OH formed in core – all H2O2 formed in film, total H2O2 is that remaining at end of pulse. OH in core only fitting parameter.

## Slide 31: Reaction Model Based upon Fast Quenching
Reactions: (kf and kd’)
H2O2 formation from ∙OH in film
H2O2 degradation by ∙OH, ∙H, O, e-
rapid quenching of ∙OH in film
formation
degradation
Notes: Add details and figure showing time quenching… spatial quenching could be added later.

## Slide 32: Model ∙OH Predictions
(Wang, Wandell, Locke, 2018)
Chart: Discharge power (Watts)
| 0.29433340000000002 | 0.49573339999999999 | 0.65533399999999997 | 0.9795334
Ar | 9.81e+18 | 1.19e+19 | 1.115e+19 | 1.205e+19
He | 4.95e+18 | 5.45e+18 | 5.55e+18 | 5.99e+18
argon
helium
Smaller size argon plasma has higher ∙OH concentration in core during pulse.
Slight increase in ∙OH with discharge power for both gases.
Data on H2O2 used to determine ∙OH in plasma using model.
<OH> = 4x1014 cm-3 in argon and 2x1014 cm-3 in helium (time averaged in pulse)
For comparison in combustion – 1014 to 1016 cm-3
Notes: Again, OH in core is the only fitting parameter.

## Slide 33: Other Model Results
(Wang et al., 2018)
Calculated H2O2 degradation rates
H2O2 model data comparison
More H2O2 degradation in argon
Argon – higher rates with electrons
Helium – higher rates with ∙OH
Degradation strongly affects net formation of H2O2
Role of liquid water is to sequester H2O2 and suppress degradation in plasma
Relative H2O2 degradation rates by electrons and ∙OH
Airity PS (frequency)
Eagle Harbor

## Slide 34: Effects of Frequency on Hydroxyl Radical (data for input to model, Airity Nanopulser)
Airity power supply, 2 mL/min, 0.25 mm inlet nozzle, 70 V delivered
Energy per pulse ranges from 80 to 140 mJ/pulse
H2O2 data: V. Babicky, M. Clupek, V. Jirasek , P. Lukes
Electron density
H2O2
(with varying input phenol concentration)
(time and space averaged electron density)

## Slide 35: Effects of Frequency on Hydroxyl Radical (model results compared with ∙OH from OES)
Chart: Frequency (kHz)
| 60 | 30 | 10 | 1
[OH]p*Frequency | 4.2e+23 | 2.4e+23 | 1.1e+23 | 1.35e+22
OH Peak Intensity | 60.77 | 35.78 | 12.69 | 1.231
Airity power supply, 2 mL/min, 0.25 mm inlet nozzle, 70V delivered
From model
OES Data
Variation in ·OH with frequency correlated with electron density variation.
∙OH measurements with time and space in progress (Vorac & Dvorak – Masaryk U.).

## Slide 36: Molecular Hydrogen Production
(Airity power supply,
S. Bresch, IPP)
H2
H2O2
in He
in He
in Ar
in Ar
In Helium
H2:O2 = 3.4
under water
H2:O2 = 4
Trend for H2 formation similar to those for ∙OH; H2 may rapidly escape plasma region.
H2O2 levels off at high frequency, likely due to degradation reactions.
Formation of O2 demonstrated from water in argon and helium carrier gases.

## Slide 37: Influence of Liquid Conductivity: H2O2 (Eagle Harbor nanopulser)
Production rate
Energy yield
Relatively small changes in H2O2 formation with large changes in liquid conductivity for nanopulser.
Large range of operation possible with nanosecond pulser but not microsecond power supply.
Argon
Argon
Helium
Helium
Microsecond power supply
100x lower

## Slide 38: Liquid phase ·OH Scavenger (Methylene Blue – a water soluble organic dye)
Chart: Flow Rate (ml/min)
| 0.75 | 1 | 1.5 | 2 | 5
OH• from H2O2 (mol/s) | 2.4993e-07 | 2.3961e-07 | 2.7094e-07 | 2.6363e-07 | 2.6067e-07
OH• from Decoloration (mol/s) | 1.0854e-09 | 1.4233e-09 | 7.5227e-11 | 2.6223e-09 | 4.2942e-09
OH• from TOC (mol/s) | 8.5487e-09 | 1.9504e-08 | 2.5338e-08 | 1.1366e-08 | 7.4906e-09
OH• production rate | (mol/s)
H2O2 from dI H2O | 2.40 ± 0.25 x 10-7
H2O2 from 0.1 mM MB | 2.57 ± 0.12 x 10-7
MB decoloration | 2.30 ± 0.13 x 10-9
MB mineralization | 1.38 ± 0.67 x 10-8
Complete MB decoloration has little effect on ·OH (H2O2) production.
MB complete degradation requires 57 moles of ·OH.
Notes: MB – liquid phase probe – concentration too low to affect H2O2 production, but OH radicals from plasma can degrade and fully oxidize MB
Problem with increasing MB concentration since it affects the conductivity of the solution which affects the discharge (at least with the ignition coil)

## Slide 39: Hydroxyl Radicals in Liquid Phase
pss
[OH]pss = 1.2 to 4.3 x10-10 M
Based upon non-volatile organic dye decoloration in liquid
Ignition coil data with argon carrier gas. (Hsieh, 2015)
For comparison - Advanced Oxidation Technologies
  ∙OH: 10-4 to 10-1 nM (quasi steady-state due to very high reactivity)

## Slide 40: OH Radical Attack with Liquid Scavenger (Methylene Blue)
gas phase
liquid phase
plasma
zone
Ar
H2O
Ar*
e-
e-
∙H ∙OH
e-
mass transfer
H2O2
MB
MB-OH
  ∙OH reacts in the liquid phase (near interface) with MB
  MB does not affect H2O2 formation (in plasma zone)
  Some ∙OH is able to go from plasma to liquid interface to degrade MB
∙OH + ∙OH  H2O2
Not drawn to scale.
Notes: Not enough MB to conclude – need to look at other probes

## Slide 41: OH Radicals from Ethanol
Overall 2 moles of ·OH to convert ethanol to acetaldehyde.
Number of ·OH independent of specific pathway.
Measure reaction product of acetaldehyde.
Underestimate due to further oxidation of acetaldehyde.
Notes: Ethanol introduced in the liquid phase – without plasma about 5% of ethanol ends up in the gas phase.

## Slide 42: ·OH Production Rate from Ethanol
·OH + ·OH → H2O2 C2H6O + ·2OH → C2H4O + 2H2O
H2O2 completely depleted by ethanol.
Acetaldehyde accounts for same amount of ∙OH as H2O2.
H2O2 likely formed in plasma zone near plasma-liquid interface.
Gas phase,
product
Notes: Mass transfer results shown earlier indicate that most of the ethanol goes to the plasma from the liquid, but some 7% of the ethanol can transfer directly into the gas.

## Slide 43: ·OH Attack with Gas/Liquid Scavenger (Ethanol)
gas phase
liquid phase
plasma
zone
Ar
H2O
Ar*
e-
e-
e-
AA
AA
EtOH
  Major product acetaldehyde, primarily collected in the gas phase.
  Ethanol can deplete H2O2 by competing fully for ∙OH.
  Ethanol can transfer into the plasma zone (unlike MB which stays in liquid).
∙OH + ∙OH  H2O2
∙H ∙OH

## Slide 44: OH Radicals from Carbon Monoxide (Gas phase reactions and probe)
Chart: Mole fraction of CO in argon (%)
| 0 | 3.9396872815426025E-3 | 5.9480081590830699E-3 | 1.3185141327064958E-2 | 2.5471107736875307E-2
OH from H2O2 (mol/s) | 1.8194e-07 | 1.6008e-07 | 1.5466e-07 | 1.4597e-07 | 1.3079e-07
OH from CO2 (mol/s) | 8.2437e-08 | 1.1801e-07 | 2.3679e-07 | 3.78e-07
CO + OH• → CO2 + H•
Significant gas phase ·OH that does not form H2O2.
·OH available for reactions with gaseous species as well as liquid.
Requires high CO to affect H2O2.
•OH + •OH
 H2O2
•OH + •H
H2O
(and other loss reactions)

## Slide 45: OH Radical Attack with Gas Scavenger (Carbon Monoxide)
gas phase
liquid phase
plasma
zone
Ar
H2O
Ar*
e-
e-
∙OH ∙H
e-
H2O2
CO
CO2
∙OH + ∙OH
 H2O2
∙OH + ∙H
 H2O
CO may be reacting with ∙OH that goes to form other species like H2O.
Large amounts of CO needed to affect H2O2 production. Supports idea that
most H2O2 is formed in plasma zone near liquid interface.
Notes: The reactions that form OH may be dependent upon the plasma properties
And the reactions that form H2O2 for example may be more dependent upon the quenching processes.

## Slide 46: Hydroxyl Radical Generation from Water
Thermodynamic limit
(from DHr)
H2O  ∙OH + ∙H
H2O + e-  ∙OH + ∙H + e-
H2O + hn  ∙OH + ∙H
H2O + e-  ∙OH + ∙H + e-
20
(120 to 190 nm, depends on quantum yields and lamp efficiencies)
2 to 4 (in liquid)
7 to 9 (in gas with vapor)
(electron beams, gamma radiation)
Yields* (molecules/100 eV)
2 to 3 (in liquid)
5 to 6 (in gas with vapor)
UV light
Radiation
Plasma
2 to 5 (exp, probes, ignition coil)
3 to 7 (exp, probes, nanopulser)
2 to 4 (model,H2O2, nanopulser)
2 to 8 (in liquid)
Over water
Underwater: (Sahni and Locke, 2006)
10-2 (primary) 2x10-1 (w/ H2O2)
Advanced Oxidation Processes
(O3, O3/UV, H2O2/O3, H2O2/UV, H2O2/Fenton)
Notes: What is the hydroxyl radical – electrically neutral, unpaired electron, when discovered etc. (throughout consider differences between gas and liquid phase reactions)
Why is the hydroxyl radical important – reaction rate constant – diffusion limits in gases and liquids – kinetics - fast rates lead to mass transfer limits
Where is the hydroxyl radical important – atmospheric chemistry, cellular biology, combustion, extraterrestrial space
How do you make hydroxyl radicals – thermal, photo, electrical, radiative – homogeneous vs heterogenous sources
What are the limitations on energy yields for hydroxyl radicals and therefore their reactions with targets?
How do you efficiency utilize hydroxyl radicals – since rate so fast can lose quickly, competing reactions
How to measure hydroxyl radicals – chemical, physical-optical-laser etc.
Role of hydroxyl radicals in plasma contacting liquid water
- other competing reactions and processes - complications
- comparison to radiation processes
- oxidation/reduction processes – oxidation vs reduction – should they balance in plasma?
- OH reactions in the liquid phase
- OH reactions in the gas phase

## Slide 47
(Bresch et al., 2015)
Hexane Oxidation
(Ignition coil, gas phase reactant)
Experiments and modeling show products due to ∙OH and ∙H reactions
Hexane fed as gas – dilute amount to prevent polymerization.
Products in liquid and gas
Quantum chemical calculations using Gaussian 03
Notes: Complex set of products observed from hexane, hexane remains in the gas primarily, but concentration used is relatively small.
Use low hexane to water ratio to prevent over oxidation and polymer formation

## Slide 48: Initial Reaction Steps
Although both ∙OH and ∙H reactions possible
∙OH reactions generally more likely based upon DG
(and products – see next slide)
(Bresch et al., 2015)
Notes: Formation of hexyl radicals by ∙H abstraction through ∙OH or ∙H. All reactions are exothermic and exergonic and will proceed at room temperature. Red enumeration: Carbon-hydrogen bond that is broken in the subsequent reaction. Calculations at B3LYP 6-311++G(d,p) level
Liquid water provides the source of OH radicals, but also provides the sink for collection of many of the reaction products. The high ratio of water to organic prevents over oxidation of organic, but still leads to wide range of products with low selectivity.

## Slide 49
(Bresch et al., PCPP, 2015)
Colored boxes –
products observed
(NMR, GCMS)
∙OH products observed
Hexane production
Distribution
Notes: All reactions proceed through formation of hexyl radicals
All pathways due to OH radicals.

## Slide 50: Post-plasma Considerations -1,4 dioxane degradation-
Example Application
Partial degradation of 1,4 dioxane by plasma
  1, 4 dioxane highly water soluble, non-volatile
  Emerging groundwater contaminant found in combination with chlorinated contaminants
Mineralization in bioreactor after plasma reactor
Seeking to improve overall efficiency by reducing overall energy cost by combining plasma for initial degradation with bioreactor for complete mineriization of products from plasma.
(Xiong et al., 2019)

## Slide 51
Plasma/Bioreactor Treatment Performance
Plasma reactor performance
Bioreactor performance
Optimum HRT in plasma reactor occurs when majority of dioxane is converted to intermediates in plasma reactor, but organic products remain
Plasma degrades 1, 4 dioxane; bioreactor degrades remaining products.
Plasma/bioreactor utilizes 5 times less power than plasma alone
and bioreactor is about 5 times faster than without plasma.
Bioreactor alone can only partially remove 1, 4 dioxane and organic carbon.
Notes: Starts from case 6 dioxane-TOC-comparision between these two

## Slide 52: Dioxane Plasma Degradation Pathway (liquid phase, ·OH based)
(boxed products detected
By GC/MS and NMR)
Products from 1, 4 dioxane suggest oxidation by ·OH.

## Slide 53: Formation of Nitrogen Oxides in Ar/N2 Liquid Phase Results
Increasing N2
  NO3- saturates and NO2- continues to increase gradually w/ N2
  Limitation of ∙OH supply likely
Increasing N2 in argon up to 3% reduces H2O2 about 25%.
  Note ∙OH is still present to form H2O2, but H2O2 not largely suppressed by high N2 (like CO probe shown previously).

## Slide 54
Gas Phase CO as ∙OH Scavenger in Ar/N2
Increasing CO:
  Does not affect NO formation
  Lowers NO2, H2O2, NO2-, and NO3-
Reactions: CO + •OH  CO2 + •H
      •OH + •OH  O + H2O (more likely source of O for NO formation)
      NO + •OH  HNO2 (decreased due to CO quenching ∙OH)
      NO2 + •OH  HNO3 (decreased due to CO quenching ∙OH

## Slide 55: Hydroxyl Radicals in Ar/N2 Plasma CO scavenging ·OH
Significantly more ∙OH in CO reactions than in total H2O2 and NOx.
  Implies room for improvement in plasma oxidation reactions
•OH energy yield 6.7 eV/100 molecules provides information on “primary” formation of ∙OH
H2O2
CO to CO2
NO
(via O from OH)

## Slide 56: Hydroxyl Radicals in Ar/N2 Plasma NO scavenging of ∙OH
NO + •OH  HNO2
•OH+ •OH  H2O + O
•OH+ •OH  H2O2
3:1 OH:HNO3
1:1 OH:HNO2
2:1 OH:NO2
2:1 OH:H2O2
Experimental data suggests ∙OH controls formation of HNO2, HNO3 and atomic oxygen
HNO2 and HNO3 production limited by back reactions with increase in inlet NO

## Slide 57: Summary of Nitrogen Species Reaction Pathways
Liquid phase
+•OHH2O2
NO2
Gas Phase
Plasma zone
NO+•OHHNO2
NO2+•OHHNO3
Flow direction
H2O2+e-•OH+•OH+e-
HNO2+•OHH2O+NO2
HNO3+•OHH2O+NO3
NO3+•OHHO2+NO2
Degradation
•OH+•OHH2O+O
NO+O NO2

## Slide 58: Conclusions
Gas-liquid reactor utilized here characterized with respect to
  Geometry of gas and liquid volumes and interface
  Hydrodynamic flow patterns, pressure, and mass transfer characteristics
  Effects of power supply type (microsecond vs nanopulser)
  Plasma gas temperature, electron density, and electron energy
  Effects of solution conductivity, pulse frequency, power supply type
    Nanopulser (fast rise) operates to near seawater conductivity without large drop in H2O2.
  Formation of hydroxyl radicals, hydrogen peroxide, oxidation products of several organic compounds including liquid phase, gas phase, and volatile compounds
Relatively high efficiency for ∙OH formation demonstrated
  ·OH (primary) energy yields comparable to all other AOPs
  ·OH reactions/reaction products found in both gas phase and liquid phase
  ·OH reactions
    Reactions of many organic compounds in the liquid and gas phases
    Control formation of nitrogen oxides, particularly formation of acids
    Control formation of hydrogen peroxide
    Degradation reactions (reverse and others) can reduce efficiencies
Notes: Nano pulse power supply provides a good system to study these factors.
Still do not know how plasma properties fully affect the measured chemical reactions.
Trade off between production rate and efficiency has the same (opposite) trends as the other systems discussed in this conference including results for CO2.

## Slide 59
Recent Collaborators
Prof. Igor Alabugin
(Chem/Biochem)
Dr. Stefan Bresch
(Chem PhD 2015)
Dr. Kevin Hsieh
(ChE PhD 2015)
Robert Wandell
(ChE PhD 2016)
Huihui Wang
(ChE PhD 2018)
Radha Bulusu
(ChE PhD candidate)
Kosuke Tachibana
(PhD, Tokyo Inst. Tech.
Oita University)
Undergraduates
  Basiel Makled
  Parastou (Mandy) Shahzeidi
  David Reece
  Rachel Gallan
  Qiao Zhang (BS/MS)
Others
  Eagle Harbor Technologies
  Patrick Breslend, FSU
  Dr. Pavel Dvorak, Masaryk Univ.
Prof. Youneng Tang
(Civil Envir. Engr.)
Yi Xiong
(CEE PhD candidate)
Prof. Radu Burlica
(Iasi Univeristy)
Institute of Plasma Physics, Prague
  Dr. P. Lukes, Dr. V. Jirasek
  Dr. V. Babicky, Dr. M. Clupek
  Dr. M. Simek
Dr. Jan Voráč
(Masaryk University)

## Slide 60
Thank you for your interest.

## Slide 61: Hydroxyl Radicals in N2/Ar Plasma
Significantly more ∙OH in CO reactions than in total H2O2 and NOx.
  Implies room for improvement in plasma oxidation reactions
•OH energy yield 6.7 eV/100 molecules provides information on “primary” formation of •OH
H2O2
CO to CO2
NO
(via O from OH)

## Slide 62: Water Plasma (electron) Interactions
e- + H2O  e-, O, H, OH
Molecules
H2Oliq
Clusters
e- +
H2Oliq
Aerosols
e- +
Plasma/gas
continuous
phase
Electron interaction with
one water molecule.
Electrons interact
with groups of water
molecules
Surfaces
e- +
H2Oliq

## Slide 63: Water Plasma (electron) Interactions
Bubbles
H2Oliq
e-
Plasma Channels
e-
H2Oliq
Liquid is
continuous
phase
Increasing photographic time exposure
Thermal or
Injected bubble
Fine bubbles
formed
Vapor bubble

## Slide 64: Treatability Ranges (adapted from Tarr, 2003)
10-2 10-1 1 101 102 103
ADVANCED
OXIDATION
BIOLOGICAL
OXIDATION
SUPERCRITICAL
OXIDATION
INCINERATION
Chemical oxygen demand (COD) g/l
Non thermal plasma
Thermal plasma

## Slide 65: Predicted generation of ·OH by various AOPs
Process | O3 | H2O2 | UV | O3 | UV | H2O2 | OH yield
 | g/kWh | g/kWh | eV/photon | mole O3/ mole OH | mole photon/ mole OH | mole H2O2/ mole OH | molecules/ 100 eV
O3 | 50 |  |  | 1.5 |  |  | 1.9
O3 | 100 |  |  | 1.5 |  |  | 3.7
O3/UV | 50 |  | 1 | 1.5 | 0.5 |  | 1.8
O3/UV | 50 |  | 6 | 1.5 | 0.5 |  | 1.8
O3/UV | 100 |  | 1 | 1.5 | 0.5 |  | 3.6
O3/UV | 100 |  | 6 | 1.5 | 0.5 |  | 3.3
O3/H2O2 | 50 | 50 |  | 1 |  | 0.5 | 2.1
O3/H2O2 | 100 | 50 |  | 1 |  | 0.5 | 3.3
H2O2/UV |  | 50 | 1 |  | 0.5 | 0.5 | 7.6
H2O2/UV |  | 50 | 6 |  | 0.5 | 0.5 | 6.4
H2O2 Fenton |  | 50 |  |  |  | 1 | 3.9
H2O2 Fenton |  | 100 |  |  |  | 1 | 7.9
Stoichiometry taken from Glaze, 1987
Does not account for low O3 solubility and mass transfer
Idealized view due to solution (pH, scavengers, etc.) conditions
assumed
estimated

## Slide 66: Hydroxyl Radicals from AOPs
Process | Overall reactions
O3 | Molecular: O3 + reactant  product Radical: O3 … ·OH
H2O2 - Fenton | H2O2 + Fe2+  Fe3+ + ·OH + OH-
O3/H2O2 | H2O2 + 2O3  2 ·OH + 3O2
UV | Reactant + hn  products
O3/UV | O3+H2O + hn  2 ·OH + O2
UV/H2O2 | H2O2 + hn  2 ·OH
O3/UV/H2O2 | 2O3 + H2O2 + hn 2 OH + 3 O2
Key species: input – O3, H2O2, UV major reactant - ·OH
Notes: Water pollution problem – emerging areas – endocrine disrupters, pharmaceuticals, personal care products, surface active species, etc….

## Slide 67: Ozone Reactions in Water
(Staehlin and Hoigne, 1985)
1) O3 + reactant  products
2) O3 … ·OH
(net 1.5 moles O3 to 1 mole ·OH)
·OH + reactant  products
Limitations
Ozone solubility in water
Mass transfer
Solution properties, e.g. scavengers
Notes: Ozone chemistry in liquids…. Hoigne, Bader, etc.

## Slide 68: UV and Chemical Pathways
(Peyton/Glaze 1988)
(Peyton 1990)
Ozone + UV
H2O2 + UV
O3+H2O + hn  2 ·OH + O2
H2O2 + hn  2 ·OH

## Slide 69: Scaled-up Prototype

## Slide 70: Oxygen Addition
Oxygen addition leads to significant ozone formation in the gas phase.
Oxygen addition only slightly decreases H2O2 formation.
Oxygen addition has no effect on MB decoloration in liquid.
  Suggests ozone transfer to liquid and reactions is liquid slow.
Ozone production
Hydrogen peroxide formation
Notes: Effect on MB data not shown here.

## Slide 71: Dye Removal
Reactor | Energy Yield g/kWh
Pulsed discharge in water | 0.08 to 0.2
DC discharges in air over water film | 4.9
Plasma jet discharge with argon | 0.4
PCD in water with O2 bubbling | 0.59
Water film reactor with argon (this work) | 2.3 to 4.0
Laminar jet with bubbling (Thagard) | 11.4
Water spray in PDBD with O2 | 45
UV/H2O2 | 0.1
Ultrasound | 0.2
Photocatalysis | 0.2
Ozonation | 0.3
Chart: Liquid Flow Rate (mL/min)
| 0.5 | 1 | 1.5 | 2
0.5 mM RhB | 30.0508 | 19.3139 | 7.2427 | 9.1487
0.1 mM MB | 8.5 | 7.15 | 4.44 | 4.05
Total Organic Carbon Removal

## Slide 72: Key issues
Can we control the chemical reactions by changing the input conditions?
  How affect efficiency and selectivity?
Do the input pulse parameters affect plasma properties such as electron density, electron temperature, and plasma temperature?
Do these plasma properties affect chemistry?
What is the role of liquid water?
  Source of reactants: from liquid to plasma
    H2O: ∙OH oxidant, H reductant
  Interface and transport of mass and energy
    Second phase improves plasma, thermal, and chemical quenching and increases gradients at phase boundary
    Magnitudes of the gradients in temperature and concentration at interface
    How do gradients affect chemical reactions?
    Which reactive species transfer between plasma and liquid?
  Collects products: from plasma to liquid
    H2O2, alcohols, aldehydes,...
Notes: First three in common with gas phase plasma systems - well studied in gas phase, but can be different with liquid phase
Last part with liquid water different – is there a difference when adding or contacting a liquid phase?
Known unknowns

## Slide 73: Summary
gas phase
liquid phase
plasma
zone
Ar
H2O
Ar*
e-
e-
∙OH ∙H
e-
mass transfer
H2O2
H2O2
∙OH + ∙OH → H2O2
∙OH + H2O2 → HO2∙ + H2O
∙OH + ∙OH → H2O + O∙
H∙ + ∙OH → H2O
Organic compounds in gas phase: hexane, CO, ethanol
Organic compounds in the liquid phase: MB, ethanol
∙OH + Organic  prod
Organic+ ∙OH
 prod

## Slide 74: Electrical Circuit Model for Conductivity Effects (Eagle Harbor nanopulser)
L
, , : Resistance of plasma, water film, and resistors in the circuit
: Capacitance of reactor
: Cross-section area of plasma channel
: Elementary charge
: Mobility of electron
: Electron density
: Electrode gap
: Inductance of wire
+
-
Pulser
R2
R1
R3
Rp(t)
Cp
Eagle Harbor Power Supply
Water Film Reactor
Rw
R4
Applied voltage:
V(t)
Vd(t)
Supply
Ne(t) – assumed to follow current pulse.
(Wang et al., 2019)

## Slide 75: Simulating Discharge Voltage and Current (Eagle Harbor nanopulser)
(Power Supply: 20 kV, 2kHz, 50ns; DI water 1mL/min; Argon)
20 ns
30 ns
DI water
DI water
7.5 kV
Breakdown voltage

## Slide 76: Liquid Conductivity and Breakdown Voltage (Eagle Harbor nanopulser)
40mS/cm KCl Solution
5 kV
Breakdown voltage
(Wang et al., 2019)
Power Supply: 20 kV, 2kHz, 50ns; 40 mS/cm, 1mL/min; Argon
Breakdown voltage drops with liquid conductivity

## Slide 77: Influence of Applied Voltage on Breakdown
5 kV
3 kV
Breakdown voltage
Conditions/Assumptions:
  40mS/cm KCl solution
  Carrier gas: Argon
  Electron density was assumed unchanged with applied voltage
  Two applied voltages with different pulse rise time were used
40mS/cm KCl Solution
Longer rise times lead to lower breakdown voltages.
Ignition coil power supply rise time 4 ms insufficient to generate discharge at high conductivity.
Eagle Harbor power supply rise time 20 ns works very well.