## Slide 1
z
ChipSat and Nanospacecraft
Orbital Lifetime Limitations
Research Question
Electrodynamic Tethers for ChipSats and Nanospacecrafts
We gratefully acknowledge support from AFOSR grant FA9550-09-1-0646
Nestor Voronka and Robert Hoyt
Tethers Unlimited, Inc.
Sven Bilén and Jesse McTernan
The Pennsylvania State University
Brian Gilchrist and Iverson Bell, III
The University of Michigan
Trade Study
Results
Background
Tether Lengths Required for Orbital Maintenance
Tether Mass and Resistance
Current Collection and Drag
Example System Concept
Performance Modeling
Using TEMPEST evaluation software
Future Work
References
A Rough Estimate of Satellite Lifetime due to Atmospheric Drag |  |  |  |  | 
Parameters | 3 kg CubeSat | 8 g ChipSat |  | 7.5 mg ChipSat | 
Configuration | 3-1000 cm3 cubes, stacked upright | Low drag | High Drag | Low Drag | High Drag
Ballistic Coeff. | 45 | 95 | 2.5 | 13.6 | 0.03
Alt = 300 km | a month | a month | hours | several days | ~
Alt = 400 km | several months | several months | days | several weeks | hours
Alt = 500 km | ~1 year | ~1-2 years | weeks | several months | hours
ChipSat Tether System Concept Parameters | 
ChipSat Dimensions | 7.5 mg, 1cm x 1cm x 25 µm
Altitude | 500 Km
ChipSat Orientation | “Ram”, i.e. large dimension perpendicular to velocity
Tether Width | ~13 µm
Tether Current | ~100 µA
Tether Resistance | 10 kΩ
Collector Vbias | +200 V
Electron Collector | 6.6 mm diameter sphere
Estimated Operated Conditions | 
Solar Cell Area | 1 cm2
Cell Efficiency | 25%
Available Power | 10 mW
I2R loss in tether | 100 µW
V­emf *I | 200 µW
Can propellantless EDT technology provide lifetime enhancement and maneuverability?
Short tethers require more current and a larger collection area, so a minimum length of 9 m is set by the collector size, which is a ~7 mm diameter sphere ( given ne = 105 cm-3 )
Tethers 1-100 meters can provide propulsion for currents in the 10-1000 microampere range
The minimum length estimate is too conservative. The 2-m EDT maintains orbit while the 10-m EDT increases altitude
An electrodynamic tether (EDT) can exploit the Lorentz force in the ionosphere to generate an electromotive force
The force required to overcome atmospheric drag involves a trade-off between current and length
EDT can be used for ChipSat lifetime enhancement and maneuverability
Nanospacecraft is a class of spacecraft ~1-10 kg
ChipSats are the next generation of miniaturization scaled down to the microchip level (~grams)
Potential Benefits:
- Utilize MEMS technology
- Inexpensive to transport to orbit
- Quick fabrication
-Capable of swarm data collection
velocity for reduced drag orientation
velocity for high drag orientation
Early ChipSat concepts have no propellant and a high Area/Mass ratio, so the orbital lifetime is very short
9 µm diameter Silica core
1.8 µm Nickel coating
~ 1 µm insulation
Tether
Cross Section
10 m
insulated
tether
Solar panel
Power supply
Electron collector
Electron emitter
ChipSat EDT material study
Further electron collection and emission studies
Micro-energy storage
Tether libration (TetherSim)
Boosting strategy to maintain circular orbits
[1] Barnhart, D., Vladimirova, T ., and Sweeting, M . “Satellite-on-a-Chip: A Feasibility Study. “ Not published, University of Surrey.
[2] Peck, M. “A Vision for Milligram-scale spacecraft,” Presentation at ChipSat Workshop 2010, Brown University. 2010.
[3] Wertz , J. and Larson, W., eds. Space Mission and Analysis and Design. 3rd Ed. Microcosm Press, 1999, pp .145.
[4] Fuhrhop, K. “Theory and Experimental Evaluation of Electrodynamic Tether Systems and Related Technologies,” University of Michigan Ph.D. Dissertation 2007, pp. 17-53.
[5] Laframboise, J. and Sonmor, L. “Current Collection by Probes and Electrodes in Space Magnetoplasmas: A Review,” Journal of Geophysics, Vol. 98 No. A1 , 1993, pp 337-357.
[6] Thompson, D., Bonifazi, C., Gilchrist, B., et al. “The Current-Voltage Characteristics of a Large Probe in Low Earth Orbit: TSS-1R Results,” Geophysics Research Letters, 1998 , pp. 413-416.
[7] Choiniere, E., Bilen, S., and Gilchrist, B. “Experimental Investigation of Electron Collection to Solid and Slotted Tape Probes in a High Speed Flowing Plasma” IEEE Transactions on Plasma Science ,Vol. 33 No. 4 , 2005, pp. 1310-1322.
[8] Fuhrhop, K. and Gilchrist B. “Optimizing Electrodynamic Tether System Performance“ AIAA Space Conference and Exposition, 2009, pp 1-17.
To limit the tether mass and resistance, the tether should be less than 10 m
8.5 m bare wire
16x16 cm2 foil
90 cm porous tape
6.6 mm diameter sphere
A 10-m EDT has 10 kΩ of resistance
A 10-m EDT has the same mass as the ChipSat
( assuming the electron density is 105 cm-3 )
10m Tether: Altitude vs. Time
2 m Tether: Altitude vs. Time