## Slide 1
Nonlinear Oscillations of Levitated Gas Bubbles and Their Impact on Plasma Formation in Water
Bradley S. Sommersa
John E. Fosterb
Presented at the 2nd Graduate Symposium of the Michigan Institute for Plasma Science and Engineering
Tuesday, May 21st, 2011
(a) Dept. of Nuclear Engineering, University of Michigan, Ann Arbor, USA, bsso@umich.edu
(b) Dept. of Nuclear Engineering, University of Michigan, Ann Arbor, USA, jefoster@umich.edu

## Slide 2: Liquid Plasma: Applications & Issues
thin electrode tips
small electrode spacing
400 μm
These issues stand as a barrier to practical implementation
Strong chemical reactivity
  UV radiation
  radicals (OH-, ozone)
  energetic electrons
Applications
  water purification
  industrial processing
Issues
  water is a very good insulator
  (Eholdoff > 1 MV/cm)
  electrode erosion (contamination)
  small throughput
  shot-to-shot variability

## Slide 3: Electric Field Effects in Water
Water acts as a “leaky dielectric”2
  dielectric permittivity (bound charge)
  finite conductivity (free charge)
Macroscopic effect of electric stress
  electric stress:
  surface tension stress:
  Weber Number:
pE
undisturbed boundary
boundary depressed by pE
bubble interior
Ē
2Garton, Krasucki, Proc. Royal Soc. Lon.., Vol. 280, No. 1381, July 21, 1964.
  For 16 kV/cm, 3 mm, WE ~ 1 (applied field)
  For 100 kV/cm, 3 mm, WE ~ 25 (streamer)

## Slide 4: A Single Bubble under an A.C. Field
Conditions
  voltage: 5kV A.C.
  frequency: 600 Hz
  electrode gap: 2.3 mm
  bubble diameter: 0.64 mm
t = 0.0 ms
Figure 5. A single oscillation cycle of a levitated bubble being driven by an A.C. electric field.

## Slide 5
E
Observations
  dramatic shape change
  oscillation frequency ~ 600 Hz
  WE ~ 0.17
t = 1.7 ms
top electrode
bottom electrode

## Slide 6: Lowering the Breakdown Threshold
Bubble shape distortion: increase E/N
  Shape effect: The permittivity gradient near the dielectric boundary refocuses and intensifies fields at areas of high curvature.
  Volume effect: Under a sufficiently fast expansion of the bubble volume, the internal gas pressure decreases according to an equation of state, (pVγ = constant)
field enhanced at dielectric boundary
drop curvature can be drastically distorted
1Azuma, H., J. Fluid Mech., Vol. 393, 1999
Conditions for plasma formation inside the bubble can be varied through externally driven distortion

## Slide 7: Previous Work
t = 0.0 ms
t = 2.5 ms
t = 5.0 ms
t = 7.5 ms
minimum deformation
expansion with streamer
maximum deformation
bubble attached to electrode, driven by 5 kV A.C. voltage
bubble oscillates near natural frequency (50 Hz)
streamer excited inside bubble
Achieved large bubble deformation, including area increase of up to 20%

## Slide 8
Bubble expands in response to the increasing field
Deformation closely resembles L =2 mode

## Slide 9
At the extremum, bubble curvature becomes sharp, indicating higher order modes. The electric field here is predicted to be intense
As the field is reduced, the bubble’s inertia compresses it beyond its equilibrium shape.

## Slide 10: Overview
Plasmas are promising for a host of environmental applications but are limited by large voltage and energy requirements.
The reduced field inside a gas bubble submerged in water can be enhanced when it undergoes severe distortions.
  shape effect: field intensification near distorted dielectric surface
  volume effect: internal pressure drop accompanying expansion
Precise levitation of air bubbles has been achieved via ultrasonic levitation
Intense distortion of suspended air bubbles driven by A.C. fields has been observed with implications for the internal reduced field
  severe curvature at bubble “tips” indicates field amplification
  substantial volume increases indicate decreases in internal pressure

## Slide 11: Experimental Approach Part I: Ultrasonic Levitation
Purpose: study isolated bubble under repeatable conditions
Physical Mechanism
  piezoelectric ceramic transfers electrical energy into acoustic energy
  acoustic standing wave established in 3-D rectangular cell
  bubble trapped at node
  coupler provides lateral stability3
  wave mode: [1,1,2]
3 Trinh, E.H., Thiessen, D.B., J. Fluid Mech., Vol. 364, 1998
Figure 1. Water filled bubble levitation chamber

## Slide 12
Chart: Frequency [kHz]
| 25.5 | 25.6 | 25.700000000000003 | 25.800000000000004 | 25.9 | 26 | 26.1 | 26.2 | 26.25 | 26.3 | 26.35 | 26.4 | 26.45 | 26.5 | 26.55 | 26.6 | 26.700000000000003 | 26.800000000000004 | 26.900000000000006 | 27 | 27.1 | 27.2 | 27.3 | 27.4 | 27.5 | 27.6 | 27.7 | 27.8
Impedance | 282.9268 | 276.1905 | 257.7778 | 246.8085 | 231.3725 | 203.5088 | 190.3226 | 152 | 131.8182 | 106.5421 | 102.6549 | 112.8713 | 146.8354 | 184.127 | 232.6531 | 290 | 429.6296 | 670.5882 | 970.2128 | 1115.3846 | 1017.8571 | 904.7619 | 838.2353 | 791.6667 | 730.7692 | 686.747 | 670.5882 | 633.3333
Chart: Frequency [kHz]
| 25.5 | 25.6 | 25.700000000000003 | 25.800000000000004 | 25.9 | 26 | 26.1 | 26.2 | 26.25 | 26.3 | 26.35 | 26.4 | 26.45 | 26.5 | 26.55 | 26.6 | 26.700000000000003 | 26.800000000000004 | 26.900000000000006 | 27 | 27.1 | 27.2 | 27.3 | 27.4 | 27.5 | 27.6 | 27.7 | 27.8
Absorbed Power | -0.090704 | -0.099253 | -0.11313 | -0.019455 | -0.028884 | 0.089669 | 0.18631 | 0.31958 | 0.70061 | 1.3356 | 2.3048 | 2.2712 | 1.8166 | 1.3813 | 0.96176 | 0.7086 | 0.49058 | 0.33919 | 0.26043 | 0.21457 | 0.1478 | 0.14054 | 0.122 | 0.096027 | 0.07868 | 0.056105 | 0.028663 | 0.028137
Maximum power is absorbed where the piezoelectric impedance is minimized
Figure 3. Piezoelectric resonance curves showing the (a) total impedance and (b) absorbed power as a function of frequency
Piezo specs
  operating frequency: 26.4 kHz
  Absorbed power: 2.3 Watts
  maximum acoustic pressure: ~ 1 atm above ambient
(a)
(b)

## Slide 13: Shape Mode Analysis
Bubble oscillations decompose naturally into spherical harmonics4
  equation of surface:
  spherical harmonic coeffcients:
Image Analysis
  convert RGB images to binary
  apply edge tracing algorithm to obtain bubble surface data
  numerially integrate to find mode coefficients
original image binary image
4 Trinh, E.H., Thiessen, D.B., J. Fluid Mech., Vol. 364, 1998

## Slide 14
Chart: Time [ms]
Figure 6. Percentage increase in cross sectional area of oscillating bubble as measured from image analysis. Volume expands under the action of the applied electric field.
baseline volume increases over several cycles
approximate applied voltage signal overlayed
equilibrium area line

## Slide 15: Experimental Approach Part II: Bubble Deformation
Translatable electrodes
Purpose: measure shape distortion from an applied electric field
Setup
  bubble injection via syringe
  degassed, deionized water
  (κ = 10 μS/m)
  A.C. voltage: 5 kV
  frequency: 100-1000 Hz
Diagnostics
  fast camera: 5000 frames per second
  Pearson coil / H.V. probe
  hydrophone
Figure 2. Photo of electrodes submerged in bubble levitation chamber

## Slide 16
Figure 4. Full setup used to drive and document suspended bubble oscillations

## Slide 17
Dominant Mode: L = 2
  previously observed under under uniform D.C. field5
  behaves like an ellipse to 1st order
Higher order modes
  at extreme deformation, bubble tips display sharp curvature
  Indicates the presence of higher order modes
sharp curvature indicates higher order modes
(a) A2 = 0.0
(b) A2 = 0.3
(c) A2 = 0.6
5Grigor, Zharov, Tech. Phys., Vol. 44, No. 8, 1999

## Slide 18
Chart: Time [ms]
L = 2 mode is observed to be dominant
Higher order modes are not observed
Figure 7. Spherical harmonic mode decomposition of oscillating bubble. Modes L = 2 - 6 shown.

## Slide 19
Acknowledgments
I would like to thank the National Science Foundation (NSF, grant # 1033141), particularly the CBET for supporting this research. I would also like to thank my advisor John Foster.
For further information
Please contact bsso@umich.edu. More information can be found at the Plasma Science and Technology Lab’s website,
http://www-ners.engin.umich.edu/lab/pstlab/