## Slide 1
PROPERTIES OF UNIPOLAR DC-PULSED MICROPLASMA ARRAYS AT INTERMEDIATE PRESSURES*
Peng Tiana), Chenhui Qua) and Mark J. Kushnera)
a) University of Michigan, Electrical Engineering & Computer Science
Ann Arbor, MI 48109-2122 USA
tianpeng@umich.edu, chenqu@umich.edu, mjkush@umich.edu
6th Annual MIPSE Graduate Student Symposium
October 2015
* Work supported by DARPA, the DOE Office of Fusion Energy Science and the National Science Foundation.

## Slide 2
University of Michigan
Institute for Plasma Science & Engr.
Introduction to Microplasma Arrays
Description of the simulation model
Simulation results and analysis
  Operating gas are Argon and Ne/Xe
  Scaling:
    Pressure
    Voltage
    Pulse Repetition Frequency (PRF)
  Mutual effect between plasma regions
  Geometry’s influences on plasma
Concluding Remarks
AGENDA
MIPSE_2015_Peng&Chenhui

## Slide 3
MICROPLASMAS AS METAMATERIAL
University of Michigan
Institute for Plasma Science & Engr.
Microplasma arrays are being investigated as metamaterials platforms. Optimizing metamaterial performance requires stringent control of microplasma properties.
Results from computational investigation of small arrays of microplasmas will be discussed with goal of metamaterial optimization.
[1] Sakai & Tachibana, Plasma Sources Sci. Technol. 21 (2012) 013001
[2] Singh et al. Nature Scientific Reports 4 : 5964 (2014)
[2]
MIPSE_2015_Peng&Chenhui
[1]

## Slide 4
MODELING OF PULSED MICROPLASMAS
The Hybrid Plasma Equipment Model (HPEM) is a modular simulator that combines fluid and kinetic approaches.
University of Michigan
Institute for Plasma Science & Engr.
Surface
Chemistry
Module
Monte Carlo Radiation Transport
Monte Carlo Ion/Neutral Transport
MIPSE_2015_Peng&Chenhui

## Slide 5
UNIPOLAR DC-PULSING
University of Michigan
Institute for Plasma Science & Engr.
Short pulses (~ 10s ns) heat electrons rapidly at leading edges.
Pulsing repetition frequency at several MHz.
MIPSE_2015_Peng&Chenhui

## Slide 6
2 x 2 ARRAY OF 4 MICROPLASMAS
University of Michigan
Institute for Plasma Science & Engr.
Sealed plasma cavity (no net gas flow), 2 x 2 symmetric configuration.
Powered electrodes are in the center separated by dielectric
Electrodes are exposed to enable unipolar pulsing.
Higher plasma density enabled through secondary electron emission and beam ionzation
10s of Torr, 10s ns DC pulse with several MHz PRF, unipolar excitation.
Ar and Ne/Xe mixtures.
MIPSE_2015_Peng&Chenhui

## Slide 7
ELECTRON DENSITY, IONIZATION SOURCES
MIN MAX
University of Michigan
Institute for Plasma Science & Engr.
Base case: Ar, 60 Torr, 10 MHz PRF, 30% duty cycle (30 ns pulse), -300 V
Peak [e]1.1 x 1014 cm-3.
Significant "exclusion zone" with expansion of cathode fall during pulse.
Beam ionization by secondary electrons is larger than by bulk.
Bulk ionization peaks where Te and [e] are largest (edge of cathode fall).
MIPSE_2015_Peng&Chenhui

## Slide 8
GAS HEATING
MIN MAX
University of Michigan
Institute for Plasma Science & Engr.
Gas heating in microplasmas is a major factor influencing scaling of plasma density
Gas is rapidly heated close to electrodes due to larger ion drift velocity approaching cathode fall.
Rarefaction caused by heating near electrode, decreases local ionization efficiency.
Profiles shown mid-pulse.
Ar, 60 Torr, -300 V, 30 ns pulse length, 10 MHz.
MIPSE_2015_Peng&Chenhui

## Slide 9
PRESSURE SCALING
Argon, -300 V, 10 MHz PRF, 30 to 80 Torr
Low pressure, low plasma density has thicker cathode fall excluding bulk plasma. Counter-intuitive result is better uniformity at high pressure.
With higher stopping power, Tgas increases with pressure.
Plasma density saturates as heating rarefies gas.
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
30 Torr
60 Torr
40 Torr
80 Torr
MIPSE_2015_Peng&Chenhui

## Slide 10
PRF AND VOLTAGE
University of Michigan
Institute for Plasma Science & Engr.
MIPSE_2015_Peng&Chenhui
Ar, 60 Torr, fixed pulse length (30 ns).
Increasing voltage and power deposition increases Tgas which rarefies gas, leading to saturation in peak electron density.
Lower PRF, lower average power reduces gas temperature and regains some loss in efficiency due to rarefaction.
Maximum [e] is largely a function of voltage x pulse width (V) product.
Extending pulse period with constant V then enables control of gas temperature.

## Slide 11
INCREASING DUTY CYCLE
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
PRF constant while increase pulse length.
Increasing pulse length will transfer plasma behavior from pulse like to DC like with lower electron density and larger cathode fall.
The threshold of transition in plasma behavior is when duty cycle D=60%.
MIPSE_2015_Peng&Chenhui

## Slide 12
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
 Ne/Xe=80/20, 60 Torr, -300 V, 5 MHz, 6 x 1013 cm-3
Ne/Xe MIXTURE: PRF
MIPSE_2015_Peng&Chenhui
Ne/Xe=80/20, 60 Torr, -300 V, constant 30 ns pulse.
Significant modulation of plasma during pulse due to formation of larger cathode fall in smaller electron density.
Electron density slightly decreases with longer pulses. Gas temperature less sensitive to pulse length due to higher thermal conductivity.

## Slide 13
Ne/Xe MIXTURE: PRESSURE
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
30 Torr
60 Torr
40 Torr
80 Torr
Ne/Xe=80/20, -300 V, 10 MHz PRF, 30 Torr to 80 Torr
Higher plasma densities (up to 1 x 1015 cm-3 at 80 Torr) enabled by Penning mixture.
Two quasi-steady state modes of operation
  Low pressure, low electron density, low gas temperature
  High pressure, high electron density, moderate gas temperature.
MIPSE_2015_Peng&Chenhui

## Slide 14
Ne/Xe PRESSURE-2 MODES
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
MIPSE_2015_Peng&Chenhui
Ne/Xe=80/20, -300 V, 10 MHz, 30ns pulse
Longer MFP at lower pressure does not confine secondary beam electrons, resulting in bulk ionization dominant glow mode.
Lower [e] produces a larger exclusion zone of cathode fall.

## Slide 15
STAGGERED VOLTAGES
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
MIPSE_2015_Peng&Chenhui
Interactions between microplasmas may be minimized by staggering pulsing of voltage.
Electron density, bulk and beam ionization are nearly the same as base case.
Interaction between plasmas may not be a strong effect.
Ar, 60 Torr, -300 V, 30 ns pulse length, 10 MHz.

## Slide 16
SHUTTING DOWN ELECTRODES
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
Electrodes are shut down to investigate their interactions.
Different pair of electrodes produce similar densities with little interactions between pairs.
Drifting electrons from other pairs produce higher electron density but are not critical for sustaining neighbors.
MIPSE_2015_Peng&Chenhui

## Slide 17
DIFFERENT ELECTRODE LENGTH
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
Electrode length: 65 m, 80m and 95m.
Longer electrodes produce more planar cathode fall, producing more uniform plasma.
Longer electrodes increase secondary electron emission which enables an increase in bulk electron density.
The enhancement in secondary electron emission will saturate due to unchanged E/N after electrodes reach a proper length.
MIPSE_2015_Peng&Chenhui

## Slide 18
Ar: 2 x 3 ARRAY
University of Michigan
Institute for Plasma Science & Engr.
Higher peak electron density due to smaller distance between electrodes.
Increased efficiency by additional sharing of metastable atoms between pixels.
Some asymmetry occurs from staggering of anode-cathode.
MIN MAX
MIPSE_2015_Peng&Chenhui
Ar, 60 Torr, -300 V, 30 ns, 10 MHz

## Slide 19
Ne/Xe: 2 x 3 ARRAY
University of Michigan
Institute for Plasma Science & Engr.
MIN MAX
Ne/Xe=80/20, 60 Torr, -300 V,10 MHz
MIPSE_2015_Peng&Chenhui
[e] pools at the center.
Bulk and beam ionization localized near electrodes.
Xe+ has similar profile as electrons – Ne+ ions localized near electrodes.
Pooling likely the result of diffuse Penning ionization (Ne* + Xe) coincident with confinement by periodic expansion of cathode falls.
[e]
3.4 x 1013 cm-3
[2 dec]
Beam Ionization
1.9 x 1021 cm-3s-1
[2 dec]
Bulk Ionization
6.8 x 1021 cm-3s-1
[2 dec]

## Slide 20
CONCLUDING REMARKS
Microplasma arrays in Ar and Ne/Xe at 10s – 100 Torr in sealed cavities maintained by ns DC pulses were investigated with goal of finding scaling laws of plasma density vs. pressure, PRF and voltage.
Gas heating in microplasmas at such pressures was found to be important in scaling as local rarefaction of the gas will decrease ionization efficiency during the pulse.
In Ar where plasma density saturates at high pressure due to increased gas temperature, longer post-pulse period (lower PRF) can decrease gas temperature while maintaining plasma density.
In Ne/Xe, Penning mixture enables plasma density up to 1015 cm-3 at 80 Torr, while at low pressure, Ne/Xe plasma operates at a bulk-dominated low gas temperature glow mode.
University of Michigan
Institute for Plasma Science & Engr.
MIPSE_2015_Peng&Chenhui