## Slide 1
Future Experiment for the Wisconsin Plasma Physics Laboratory (WIPPL)
*This work is funded by the U.S. Department of Energy, Fusion Energy Sciences under award DE-SC0021288
K. Bryant1, C.C. Kuranz1, J. R. Olson2, C. Forest2
1University of Michigan, Ann Arbor. 2University of Wisconsin, Madison.
How can we learn about Interplanetary Coronal Mass Ejections (ICMEs) in a laboratory environment?
What is an ICME and why are they important?
ICMEs are the source of geomagnetic storms
  Often accompanied by a shock, pushes a sheath of plasma to high energies
Geomagnetic storms caused by the sun can damage human electrical systems
We’ve designed a scaled experiment to be conducted on the Big Red Ball
~1m
Image by Doug Endrizzi
The CT is generated and shot using a CT Injector (CTI)
A Compact Torus (CT) of plasma will be sent through a perpendicularly magnetized plasma
We control the background plasma parameters to scale the experiment appropriately
The Big Red Ball
Helmholtz coils
We’re installing a ring to mount the CTI at the best location
Current flows through the outer conductor, arcs through the plasma and to the center electrode
Magnetic pressure forces plasma down the tube
Towards the end, the magnetic field reconnects, and the plasma is sent into the vessel
Ideally, we want to mount the CTI perpendicular to the Helmholtz field
A ring will be inserted between the hemispheres of the vessel with ports to mount the CTI