## Slide 1
Far-Field Measurements of a Rotating Magnetic Field Thruster
Tate Gill, Christopher Sercel, Joshua Woods, and Benjamin Jorns
Introduction
Results
Discussion
Conclusions & Future Work
University of Michigan, Department of Aerospace Engineering, Ann Arbor, MI 48109
Phenomenological Efficiency Model
= total jet efficiency
= impulse
= input neutral mass
= energy input from RMF
Objectives
Develop a phenomenological efficiency model to describe the loss mech-anisms in an RMF thruster system.
Establish the role of these different efficiency losses in our RMF test article using plasma diagnostic techniques.
Flow [mg/s] | [J] | [J] | [J] | [J]
2.7 | 11.8 ± 0.5 | 1.0 ± 0.2 | 0.15 | 0.8 ± 0.2
4.0 | 15.6 ± 0.2 | 1.5 ± 0.2 | 0.23 | 1.6 ± 0.4
5.4 | 21.3 ± 0.1 | 2.1 ± 0.5 | 0.31 | 3.2 ± 0.7
Flow [mg/s] |  |  |  | 
2.7 | 11.8 ± 0.5 | 1.0 ± 0.2 | 0.15 | 0.8 ± 0.2
4.0 | 15.6 ± 0.2 | 1.5 ± 0.2 | 0.23 | 1.6 ± 0.4
5.4 | 21.3 ± 0.1 | 2.1 ± 0.5 | 0.31 | 3.2 ± 0.7
The rotating magnetic field (RMF) drive is an inductive pulsed plasma thruster (IPPT) architecture that promises favorable scaling above 100 kW [1]
IPPTs have demonstrated efficiencies of over 50% and have been the focus of several experimental efforts [2, 3]
Performance measurements of RMF thrusters remain below theoretical predictions with < 10% efficiency [4, 5]
Thruster Operation
Antennas fire in sequence to spin up RMF ()
RMF induces axial electron plasma currents and fully ionizes gas
Axial currents couple to radial fields which drives azimuthal electron current
Azimuthal current pushes off radial bias field and accelerates plasma via the Lorentz force ()
Phenomenological Efficiency Model
Divergence
Experimental Setup
Inductive B-dot probes
Langmuir probe
Faraday probe
Retarding Potential Analyzer
Pearson coils
Near unity mass utilization and acceleration efficiencies
RMF is sufficiently ionizing and accelerating propellant
Low plasma efficiency ~10%
90% of energy coupled into plasma is lost
References
[1] K. A. Polzin, et al., Aerospace 7(8), 105 (2020).
[2] P. G. Mikellides and C. Neilly, J. Prop. Power 23(1), 51-58 (2007).
[3] K.A. Polzin, J. Prop. Power 27(3), 512-531 (2011).
[4] T. E. Webber, U. of Washington Thesis. (2010)
[5] C. L. Sercel, et al., AIAA Prop. and Energy 2021 Forum. (2021).
[6] J. Brackbill, et al., J. Prop. Power 30, 1450–1458 (2014)
Work supported by NASA NSTGRO grant number 80NSSC20K1168 and NASA NSTRF grant number 80NSSC18K1190
  Plasma Efficiency
  Thermal and magnetic energy in plasma is a lower bound estimate
  is physically representative measure
  Ionization energy is a relatively small cost < 0.15% absorbed ()
  Radiation losses from excitation collisions are significant factor (4e18 m-3 measured)
  Mass Utilization
  Mass utilization efficiencies on the order of 100% contradict previous hypothesis from numerical work [6]
  Neutral mass lost because of low duty cycle (1%) not accounted for mass utilization
  Toroidal shape of FP measurement is evidence for magnetic field reversal
  Two ion populations may be present
    Fast inductively driven
    Slower charge exchange from downstream neutral collisions
  The performance and energy flow in our RMF test article has been experimentally characterized. Mass utilization efficiency was measured above 90% for all measured flowrates and plasma efficiency was measured on the order of 10% indicating vast majority of RMF energy lost though other channels.
  Future Work
  Further characterize energy loss in the near-field
  Additional measurements of radiative, wall, and anomalous wave losses
  Visualization of ion/neutral dynamics
Mass Utilization
Coupling
Plasma
Acceleration
Contact Tate Gill
tategill@umich.edu