## Slide 1
Homogeneous vs. Plasma Chemistry in High Temperature Methane DBDs:
A Global Kinetic and Graph Theory Analysis
Acknowledgements
1
8
Penetration depth (H20) ~ 2.5 n
Motivation
Experimental Approach
Conclusions
Simulation Approach
Results
Carbon-efficient upgrading of natural gas into higher-order species
Non-thermal plasmas offer opportunity to create key intermediates from light hydrocarbons at ambient conditions
Goal:
Understand competition between temperature-dependent plasma-driven and homogeneous reaction chemistry at high temperatures
Cylindrical flow-through reactor with an integrated dielectric barrier discharge (DBD)
Reactions run at 1 atm pressure with bulk temperature controlled from 400 to 700 ℃, held at constant power
Reaction products characterized using gas chromatography (GC)
Schematic of the reactor setup for electrical characterization of the plasma and product formation analysis
CH4 + Gas → C2 Products
Reaction of interest:
This work was supported by the U.S. Department of Energy by National Energy Technology Laboratory under Award Number DE-FE0031862 and the Office of Naval Research under Award Numbers N00014-23-1-2445 and N00014-25-1-2226.
Increased temperature inhibits CH4 conversion for DBD plasma-driven reactions3
Simulations closely match experimental results and show CH4 conversion inhibition
Temperature-dependent change in distribution of C2 products from triple carbon-carbon bonding to single carbon-carbon bonding
Reduction in graphical network by importance of edge betweenness centrality provides insight into key reaction pathways and mechanisms
Increase in temperature leads to inhibition of CH4 conversion in DBD reactor
Temperature-dependent change in product selectivity and coupling of carbon
Homogeneous reaction chemistry, not plasma-driven reactions, is responsible for change to reaction mechanism at high temperatures
Results
1 Department of Aerospace and Mechanical Engineering, University of Notre Dame, Indiana 46556 USA
2 Department of Chemical and Biomolecular Engineering, University of Notre Dame, Indiana 46556 USA
Ibukunoluwa Akintola1, Jinyu Yang1, Mikhail Vasilev1, David B. Go1,2
1Pancheshnyi, S., Eismann, B., Hagelaar, G., & Pitchford, L. (2008). ZDPlasKin: a new tool for plasmachemical simulations. Bulletin of the American Physical Society, 53.
2Hagberg, A., Swart, P.J. and Schult, D.A. (2008). Exploring network structure, dynamics, and function using NetworkX (No. LA-UR-08-05495; LA-UR-08-5495). Los Alamos National Laboratory (LANL), Los Alamos, NM (United States)
3Akintola, I., Rivera-Castro, G., Yang, J., Secrist, J., Hicks, J. C., Veloso, F., & Go, D. B. (2023). Temperature inhibition of plasma-driven methane conversion in DBD systems. Plasma Chemistry and Plasma Processing, 43(6), 1999-2016.
References
Pulsed E/N and Ne every 25 𝜇s for total simulation time of 1 ms to model experimental frequency (~ 20 kHz) and filamentary behavior
Reaction model for pure CH4 consists of 29 species, 61 electron-driven reactions and 125 homogeneous reactions
NetworkX used to graph reaction network2
3-Body CH4 production reactions:
Reduced network shows reactions that create CH4 become more important at 700 ℃
C4H10, C3H8, and C2H4 are key intermediates in the CH4 conversion reaction mechanism
www.texasstandard.org
Full and reduced networks for pure CH4 plasma at 400 and 700 ℃
400 ℃
700 ℃
ZDPlasKin 0-D plasma kinetic solver used to determine time evolution of key reaction species1
Simulated reduced electric field E/N of 100 Td estimated from experimental reactor geometry and electron density Ne of 5 × 1013 cm-3 estimated from total current per half cycle electrical measurements
Simulated E/N to model frequency of plasma current activity